|  | Heathkit Cross Reference |  |  |  |  | Updated 11/12/02 |
| --- | --- | --- | --- | --- | --- | --- |
| Heath P/N |  | Generic P/N |  |  |  |  | Alternate 1 |  |  |  | Alternate 2 |  |  |  | Description |
| Signal Diode |
| 56-4 |  |  | HD2257 |  |  |  |  |  |  |  |  |  |  |  | Hughes Crystal Diode |
| 56-5 |  |  | HD6226 |  |  |  |  |  |  |  |  |  |  |  | Hughes Crystal Diode |
| 56-6 |  |  | 1N710 |  |  | 1N754 |  |  |  |  |  | 6.8 V Zener |
| 56-7 |  |  | 1N2326 |  |  |  |  |  |  |  |  |  |  |  | 1.0 V 100mA Germanium V-Ref |
| 56-8 |  |  | ED-5 |  |  |  |  |  |  |  |  |  |  |  | Erie Crystal Diode |
| 56-9 |  |  | 1N294 |  |  |  |  |  |  |  |  |  |  |  | Crystal Diode |
| 56-10 |  |  | G247 |  |  |  |  |  |  |  |  |  |  |  | 47pF Varactor |
| 56-11 |  |  | 1N60A |  |  |  |  |  |  |  |  |  |  |  | Crystal Diode |
| 56-12 |  |  | 1N2940 |  |  |  |  |  |  |  |  |  |  |  | Crystal Diode |
| 56-13 |  |  | 1N5943A |  |  | 1N5370A |  |  |  |  |  | 56 V Zener |
| 56-16 |  |  | 1N751A |  |  | 1N5231B |  | 1N4733A |  | 5.1 V Zener |
| 56-17 |  |  | STD633 |  |  |  |  |  |  |  |  |  |  |  | Tunnel Diode |
| 56-19 |  |  | 1N757A |  |  | VR9.1 |  | 1N5239B |  | 9.1 V Zener |
| 56-20 |  |  | 1N295 |  |  | 1N295S |  | 1N60H |  | 40V 35mA Germanium |
| 56-24 |  |  | 1N458 |  |  |  |  |  |  |  |  |  |  |  | 150 PIV 100 mA Switching |
| 56-25 |  |  | 1N4166A |  |  | 1N4744 |  |  |  |  |  | 15V Zener |
| 56-26 |  |  | 1N191 |  |  |  |  |  |  |  |  |  |  |  | 90 PIV 5 mA Germanium |
| 56-27 |  |  | S160 |  |  |  |  |  |  |  |  |  |  |  | 1500V 12A DO-4 |
| 56-29 |  |  | VR110 |  |  |  |  |  |  |  |  |  |  |  | 110V Zener |
| 56-31 |  |  | PS18775 |  |  |  |  |  |  |  |  |  |  |  | 6.8 V Zener |
| 56-32 |  |  | VR13.5 |  |  |  |  |  |  |  |  |  |  |  | 13.5 V Zener |
| 56-33 |  |  | 1N3754 |  |  |  |  |  |  |  |  |  |  |  | 100 PIV 0.13A Switching |
| 56-35 |  |  | 1N4951 |  |  |  |  |  |  |  |  |  |  |  | Dual Diode (Common Cathode) |
| 56-36 |  |  | VR16.1 |  |  |  |  |  |  |  |  |  |  |  | 16.1 V Zener |
| 56-44 |  |  | 1N4653 |  |  |  |  |  |  |  |  |  |  |  | 4.7 V Zener |
| 56-45 |  |  | VR20 |  |  |  |  |  |  |  |  |  |  |  | 20 V Zener |
| 56-46 |  |  | 1N4739A |  |  | 1N5239B |  |  |  |  |  | 9.1 V Zener |
| 56-47 |  |  | MZ1000-23 |  |  |  |  |  |  |  |  |  |  |  | 27 V Zener |
| 56-48 |  |  | BZT110A |  |  | 1N3814 |  | 1N5379B |  | 110 V Zener 15 mA |
| 56-49 |  |  | MV1638 |  |  |  |  |  |  |  |  |  |  |  | 30-36pF Varactor Diode |
| 56-50 |  |  | DO-7 |  |  | 5D20 |  |  |  |  |  | 2000 PIV 5mA DO-7 |
| 56-54 |  |  | VRS-5A |  |  |  |  |  |  |  |  |  |  |  | 5V Zener |
| 56-55 |  |  | VR36A |  |  |  |  |  |  |  |  |  |  |  | 36 V Zener |
| 56-56 |  |  | 1N4149 |  |  | 1N4148 |  |  |  |  |  | 100 PIV 10mA Switching |
| 56-57 |  |  | 1N716A |  |  |  |  |  |  |  |  |  |  |  | 12 V Zener |
| 56-58 |  |  | 1N709A |  |  |  |  |  |  |  |  |  |  |  | 6.2 V Zener |
| 56-59 |  |  | 1N750A |  |  | 1N5230B |  | 1N4732A |  | 4.7 V Zener |
| 56-61 |  |  | STB620 |  |  |  |  |  |  |  |  |  |  |  | Stabistor (IG-1271) |
| 56-63 |  |  | MZ500-10 |  |  |  |  |  |  |  |  |  |  |  | 5.6 V Zener |
| 56-64 |  |  | MZ1000-24 |  |  |  |  |  |  |  |  |  |  |  | 30 V Zener |
| 56-66 |  |  | VR43 |  |  | 1N3035 |  |  |  |  |  | 43 V Zener |
| 56-67 |  |  | VR10A |  |  |  |  |  |  |  |  |  |  |  | 10 V Zener |
| 56-68 |  |  | ZVR-68 |  |  | 1N5945A |  | 1N5373A |  | 68 V Zener |
| 56-71 |  |  | 1N825A |  |  |  |  |  |  |  |  |  |  |  | 6.2V Temp Comp Zener Diode |
| 56-72 |  |  | 1N4755A |  |  |  |  |  |  |  |  |  |  |  | 6 V Voltage Reference Diode |
| 56-73 |  |  | MZ2360 |  |  |  |  |  |  |  |  |  |  |  | 0.65 Forward Voltage Ref |
| 56-74 |  |  | MZ2362 |  |  |  |  |  |  |  |  |  |  |  | 2.00 Forward Voltage Ref |
| 56-75 |  |  | 1N5338B |  |  |  |  |  |  |  |  |  |  |  | 5.1 V Zener |
| 56-76 |  |  | 1N972B |  |  |  |  |  |  |  |  |  |  |  | 30 V Zener |
| 56-77 |  |  | FV1010 |
| 56-78 |  |  | FH6259 |
| 56-79 |  |  | R4507-5 |
| 56-82 |  |  | 1N3996A |  |  |  |  |  |  |  |  |  |  |  | 5.1V Zener Diode 10W Stud-Mtg |
| 56-84 |  |  | 1N4148 |  |  |  |  |  |  |  |  |  |  |  | 100 PIV 10mA Switching |
| 56-85 |  |  | SZ5.0 |  |  |  |  |  |  |  |  |  |  |  | 5.0 V Zener |
| 56-86 |  |  | FD777 |  |  |  |  |  |  |  |  |  |  |  | 15 PIV 50mA RF |
| 56-87 |  |  | FH1100 |  |  | 1N5390 |  |  |  |  |  | 5 PIV "Hot Carrier" 890MHz |
| 56-89 |  |  | GD510 |  |  |  |  |  |  |  |  |  |  |  | 25 PIV 100mA Germanium |
| 56-90 |  |  | 1N4742A |  |  |  |  |  |  |  |  |  |  |  | 12 V Zener |
| 56-91 |  |  | 1N823A |  |  |  |  |  |  |  |  |  |  |  | 6.2 V Zener |
| 56-93 |  |  | FD333 |  |  |  |  |  |  |  |  |  |  |  | 125 V 150mA RF |
| 56-94 |  |  | Selected Zener |  |  |  |  |  |  |  |  |  |  |  | 12.8 V @ 12 mA |
| 56-97 |  |  | VR7.5 |  |  | 1N3017 |  |  |  |  |  | 7.5 V Zener |
| 56-99 |  |  | 1N5223B |  |  |  |  |  |  |  |  |  |  |  | 2.7 V Zener |
| 56-602 |  |  | Unspecified |  |  |  |  |  |  |  |  |  |  |  | 10 V PIV 200mA Germanium |
| 56-604 |  |  | 1N4752A |  |  |  |  |  |  |  |  |  |  |  | 33 V Zener |
| 56-605 |  |  | 1N4746A |  |  |  |  |  |  |  |  |  |  |  | 18 V Zener |
| 56-606 |  |  | 1N5353B |  |  |  |  |  |  |  |  |  |  |  | 16 V Zener |
| 56-607 |  |  | 1N82AG |  |  |  |  |  |  |  |  |  |  |  | Silicon diode UHF Mixer |
| 56-608 |  |  | Unspecified |  |  |  |  |  |  |  |  |  |  |  | 9.1 V Zener |
| 56-612 |  |  | 1N5229B |  |  |  |  |  |  |  |  |  |  |  | 4.3 V Zener |
| 56-613 |  |  | MV2110 |  |  |  |  |  |  |  |  |  |  |  | 35-43pF Varactor Diode |
| 56-616 |  |  | 1N5232B |  |  |  |  |  |  |  |  |  |  |  | 5.6 V Zener |
| 56-617 |  |  | 1N5277B |  |  |  |  |  |  |  |  |  |  |  | 160 V Zener |
| 56-619 |  |  | 1N4733A |  |  |  |  |  |  |  |  |  |  |  | 5.1 V Zener |
| 56-620 |  |  | 1N4744 |  |  |  |  |  |  |  |  |  |  |  | 15 V Zener |
| 56-621 |  |  | 1N4738A |  |  |  |  |  |  |  |  |  |  |  | 8.2 V Zener |
| 56-626 |  |  | Selected Zener |  |  |  |  |  |  |  |  |  |  |  | 56 V Zener 8mA |
| 56-627 |  |  | 1N4741 |  |  |  |  |  |  |  |  |  |  |  | 11 V Zener |
| 56-628 |  |  | BY206 |  |  |  |  |  |  |  |  |  |  |  | 600PIV 1A Fast Recovery Diode |
| 56-629 |  |  | BZX83C3V |  |  |  |  |  |  |  |  |  |  |  | 3V Zener |
| 56-630 |  |  | 1N4748A |  |  | 1N5933A |  |  |  |  |  | 22 V Zener |
| 56-634 |  |  | 2EZ82D5 |  |  | 1N5947A |  | 1N5375A |  | 82 V Zener |
| 56-636 |  |  | 5082-2811 |  |  | HP-5082 |  |  |  |  |  | 15V 20mA Schottky Diode |
| 56-637 |  |  | PS18775 |  |  |  |  |  |  |  |  |  |  |  | 6.8 V Zener |
| 56-640 |  |  | MV2110 |  |  |  |  |  |  |  |  |  |  |  | 35-43pF Varactor Diode |
| 56-642 |  |  | MV2107 |  |  |  |  |  |  |  |  |  |  |  | 22 pF Varactor Diode (at 4.0V) |
| 56-646 |  |  | BA-244 |  |  |  |  |  |  |  |  |  |  |  | 35 PIV 100A DO-35 |
| 56-648 |  |  | MV109 |  |  |  |  |  |  |  |  |  |  |  | 26-32pF Varactor Diode |
| 56-652 |  |  | 1N4448 |  |  |  |  |  |  |  |  |  |  |  | 75V 0.45A High Speed Switching |
| 56-653 |  |  | Selected Zener |  |  |  |  |  |  |  |  |  |  |  | 91 V Zener |
| 56-655 |  |  | 1N6263 |  |  | SD101A |  |  |  |  |  | 60 PIV 15mA Schottky |
| 56-659 |  |  | 1N5998B |  |  |  |  |  |  |  |  |  |  |  | Selected Zener 8.2 V |
| 56-669 |  |  | 1N5524D |  |  |  |  |  |  |  |  |  |  |  | 5.6 V Zener |
| 56-674 |  |  | MV209 |  |  |  |  |  |  |  |  |  |  |  | 26-32pF Varactor Diode |
| 56-675 |  |  | MPN3404 |  |  |  |  |  |  |  |  |  |  |  | 20 PIV 10 mA Switching Diode |
| 56-695 |  |  | LM385Z-2.5 |  |  |  |  |  |  |  |  |  |  |  | 2.5V Zener Micro-Power TO-92 |
| 56-876 |  |  | MBD201 |  |  |  |  |  |  |  |  |  |  |  | K Band UHF/Micro TO-92 |
| Rectifier Diode |
| 57-1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Selenium Rectifier 250 PIV |
| 57-2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 65 mA Half Wave Sel Rectifier |
| 57-6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Selenium Rectifier 450 PIV |
| 57-7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Dual Half Wave Sel Rectifier |
| 57-11 |  |  | CX2C2D |  |  | Bradley CS2C2D437 |  |  |  |  |  | Selenium Rectifier |
| 57-12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Bridge Rectifier 150 PIV 150mA |
| 57-13 |  |  | Sarkes Model 50 |  |  |  |  |  |  |  |  |  |  |  | Selenium Rectifier 200 PIV |
| 57-15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 100 mA 130 PIV |
| 57-16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 100 mA 175 PIV |
| 57-17 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 500 mA |
| 57-18 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 20 Amp |
| 57-20 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 500 mA |
| 57-21 |  |  | Unspecified |  |  |  |  |  |  |  |  |  |  |  | 150 mA |
| 57-22 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 10 mA 130 PIV Selenium Recti |
| 57-23 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 200 mA 200 PIV |
| 57-25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 65 mA 130 PIV |
| 57-27 |  |  | 1N2071 |  |  | 1N4005 |  |  |  |  |  | 600 PIV 1A Rectifier |
| 57-29 |  |  | U-131 |  |  |  |  |  |  |  |  |  |  |  | Silicon Diode (Selected) |
| 57-34 |  |  | 1N3491 |  |  |  |  |  |  |  |  |  |  |  | 400V 25A Rectifier |
| 57-40 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | SCR |
| 57-42 |  |  | 3A1 |  |  | 1N5403 |  |  |  |  |  | 300 PIV 3A Rectifier |
| 57-46 |  |  | DRS102 |  |  |  |  |  |  |  |  |  |  |  | 600V 1A DO-41 |
| 57-50 |  |  | TIC44 |  |  | TI1001 |  |  |  |  |  | 30V 800mA SCR TO-92 |
| 57-51 |  |  | TIC47 |  |  |  |  |  |  |  |  |  |  |  | 200V 800mA SCR TO-92 |
| 57-52 |  |  | DO-7 |  |  | 5D20 |  |  |  |  |  | 2000 PIV 5mA DO-7 |
| 57-56 |  |  | SCM-30 |  |  |  |  |  |  |  |  |  |  |  | 3000 PIV 5mA DO-7 |
| 57-57 |  |  | GRS7PH280BAB |
| 57-58 |  |  | 40642 |
| 57-59 |  |  | 40643 |
| 57-60 |  |  | 40644 |
| 57-64 |  |  | DRS-110 |  |  | 1N4007 |  |  |  |  |  | 1000V 1A DO-41 |
| 57-65 |  |  | 1N4002 |  |  |  |  |  |  |  |  |  |  |  | 100 PIV 1A Rectifier |
| 57-67 |  |  | 10A20 |  |  |  |  |  |  |  |  |  |  |  | Full Wave Bridge |
| 57-71 |  |  | 1N825A |  |  |  |  |  |  |  |  |  |  |  | 6.2V Temp Comp Zener Diode |
| 57-84 |  |  | 45412 |  |  | 1N5759A |  |  |  |  |  | DIAC |
| 57-85 |  |  | 40668 |  |  |  |  |  |  |  |  |  |  |  | TRIAC |
| 57-86 |  |  | SPS135 |  |  | NL576A |  |  |  |  |  | SCR |
| 57-88 |  |  | MDA990-2 |  |  |  |  |  |  |  |  |  |  |  | 100V 30A FW Bridge Rectifier |
| 57-89 |  |  | MR1122 |  |  |  |  |  |  |  |  |  |  |  | 200 PIV 12A DO-203 |
| 57-91 |  |  | 41018 |
| 57-94 |  |  | 41021 |
| 57-95 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Diode Bridge |
| 57-99 |  |  | 2N6151 |  |  |  |  |  |  |  |  |  |  |  | Triac |
| 57-602 |  |  | S3900MF |
| 57-603 |  |  | S3901M |
| 57-604 |  |  | SR711A |  |  |  |  |  |  |  |  |  |  |  | Dual Diode Common Anode TO-3 |
| 57-607 |  |  | 1N5817 |  |  |  |  |  |  |  |  |  |  |  | 20 PIV 1A Schottky Rectifier |
| 57-608 |  |  | 1N5831 |  |  |  |  |  |  |  |  |  |  |  | 25 A Shottky rectifier (Stud) |
| 57-609 |  |  | 1N5393 |  |  |  |  |  |  |  |  |  |  |  | 200 PIV 1.5 A |
| 57-610 |  |  | FM-50 |  |  |  |  |  |  |  |  |  |  |  | 6000 PIV 3 mA |
| 57-612 |  |  | T2302F |  |  | H103SG |  |  |  |  |  | Triac |
| 57-614 |  |  | MR-508 |  |  |  |  |  |  |  |  |  |  |  | 800 PIV 3 A |
| 57-615 |  |  | MBS4991 |  |  |  |  |  |  |  |  |  |  |  | Bilateral Switch |
| 57-621 |  |  | MBS4992 |  |  |  |  |  |  |  |  |  |  |  | Diac |
| 57-624 |  |  | 2N5061 |  |  |  |  |  |  |  |  |  |  |  | 60V 500mA SCR TO-92 |
| Assemblies |
| 100-1727 |  |  | Temp Sensor |  |  |  |  |  |  |  | New Stock Available |  | Temp Sensor for ID-4001/5001 |
| 100-1728 |  |  | Temp Sensor |  |  |  |  |  |  |  | New Stock Available |  | Temp Sensor for ID-4001/5001 |
| Solid-State Tube |
| 150-57 |  |  | TR-1002 |  |  |  |  |  |  |  |  |  |  |  | Solid-State "6AL5" Replcmnt |
| 150-58 |  |  | TR-1119 |  |  |  |  |  |  |  |  |  |  |  | Solid-State "12AU7" Replcmnt |
| Display |
| 411-89 |  |  | FND500 |  |  |  |  |  |  |  |  |  |  |  | 7-Seg Display Common Cathode |
| 411-264 |  |  | NL905S |  |  | B-5859S |  | NL1220 |  | "Nixie" Display tube |
| 411-281 |  |  | SP-733 |  |  |  |  |  |  |  |  |  |  |  | Sperry/Beckman 3 Digit Display |
| 411-284 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | "Nixie" Display tube |
| 411-286 |  |  | SP-352 |  |  |  |  |  |  |  |  |  |  |  | Sperry/Beckman 2 Digit Display |
| 411-290 |  |  | SP-353 |  |  |  |  |  |  |  |  |  |  |  | Sperry/Beckman 3 Digit Display |
| 411-295 |  |  | SP-352 |  |  |  |  |  |  |  |  |  |  |  | Sperry/Beckman 2 Digit Display |
| 411-807 |  |  | TIL308 |  |  |  |  |  |  |  |  |  |  |  | BCD Display Driver LED |
| 411-819 |  |  | FND500 |  |  |  |  |  |  |  |  |  |  |  | 7-Seg Display Common Cathode |
| 411-823 |  |  | FND507 |  |  |  |  |  |  |  |  |  |  |  | 7-Seg Display Common Anode |
| 411-825 |  |  | FND367 |  |  | FND5141 |  |  |  |  |  | 7-Seg Display Common Cathode |
| 411-831 |  |  | TIL-312 |  |  |  |  |  |  |  |  |  |  |  | 7-Seg Display |
| 411-835 |  |  | 5082-7760 |  |  |  |  |  |  |  |  |  |  |  | 7-Seg Display Common Cathode |
| 411-836 |  |  | Futaba 4BT-04 |  |  |  |  |  |  |  |  |  |  |  | LCD Clock Display (4 Digit) |
| 411-843 |  |  | Beckman 739-02050 |  |  | Hamlin 3933-363-159 |  | AND FE0203 |  | LCD Display (3 1/2 Digit) |
| 411-859 |  |  | DS108 |  |  | 5082-7756 |  |  |  |  |  | +.1. Display Common Cathode |
| 411-860 |  |  | 5082-7760 |  |  |  |  |  |  |  |  |  |  |  | 7-Seg Display Common Cathode |
| 411-875 |  |  | MAN- |  |  |  |  |  |  |  |  |  |  |  | 7-Sec Display Common Anode |
| 411-885 |  |  | FND500 |  |  |  |  |  |  |  |  |  |  |  | 7-Seg Display Common Cathode |
| Display |
| 412-66 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Lamp IG-18 /IG-5218 |
| 412-79 |  |  | TIL209 |
| 412-616 |  |  | FLV117 |  |  |  |  |  |  |  |  |  |  |  | LED T 1 3/4 Red |
| 412-621 |  |  | Custom Lamp |  |  |  |  |  |  |  |  |  |  |  | 5V 120 mA 20,000 Hr T-1 Wedge |
| 412-633 |  |  | 5082-4484 |  |  |  |  |  |  |  |  |  |  |  | LED |
| 412-634 |  |  | 5082-4670 |  |  | HLMP-0501 |  |  |  |  |  | LED |
| 412-635 |  |  | TIL32 |  |  | QEC113 |  |  |  |  |  | IR LED T1 |
| 412-640 |  |  | LST5053 |  |  |  |  |  |  |  |  |  |  |  | LED |
| 412-644 |  |  | LST71 |  |  |  |  |  |  |  |  |  |  |  | LED (Red/Green) |
| 412-646 |  |  | 151B |  |  |  |  |  |  |  |  |  |  |  | LED |
| 412-647 |  |  | 251B |  |  |  |  |  |  |  |  |  |  |  | LED |
| 412-648 |  |  | SL247504 |  |  |  |  |  |  |  |  |  |  |  | 4 Digit Display |
| 412-654 |  |  | HLMP-1002 |  |  |  |  |  |  |  |  |  |  |  | LED |
| 412-657 |  |  | HLMP-504 |
| Transistor |
| 417-1 |  |  | 2N109 |  |  |  |  |  |  |  |  |  |  |  | PNP 35V 150 mA TO-40 (Ger) |
| 417-2 |  |  | 2N252 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 10mA TO-22 (Ger) |
| 417-3 |  |  | 2N253 |  |  |  |  |  |  |  |  |  |  |  | NPN 12V 5mA TO-22 (Ger) |
| 417-4 |  |  | 2N254 |  |  |  |  |  |  |  |  |  |  |  | NPN 20V 5mA TO-22 (Ger) |
| 417-5 |  |  | 2N238 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 10mA TO-22 (Ger) |
| 417-6 |  |  | 2N185 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 100mA TO-22 (Ger) |
| 417-7 |  |  | 2N308 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 5mA TO-22 (Ger) |
| 417-8 |  |  | 2N309 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 5mA TO-22 (Ger) |
| 417-11 |  |  | 2N1108 |  |  |  |  |  |  |  |  |  |  |  | PNP 16V 5 mA (Ger) |
| 417-12 |  |  | 2N1110 |  |  |  |  |  |  |  |  |  |  |  | PNP 16V 5 mA (Ger) |
| 417-13 |  |  | 2N1111 |  |  |  |  |  |  |  |  |  |  |  | PNP 16V 5 mA (Ger) |
| 417-14 |  |  | 2N373 |  |  |  |  |  |  |  |  |  |  |  | PNP 15V 100mA (Ger) |
| 417-15 |  |  | 2N374 |  |  |  |  |  |  |  |  |  |  |  | PNP 15V Hi Speed (Ger) |
| 417-16 |  |  | 2N544 |  |  |  |  |  |  |  |  |  |  |  | PNP 35V 10mA TO-7 (Ger) |
| 417-17 |  |  | R-250 |
| 417-18 |  |  | 2N408 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 70mA TO-1 (Ger) |
| 417-19 |  |  | R-270 |
| 417-20 |  |  | 2N2553 |  |  | R265A |  | 2N1039-1 |  | PNP 40V 3A Str-10 (Ger) |
| 417-21 |  |  | 2N1274 |  |  |  |  |  |  |  |  |  |  |  | PNP 25V 50mA TO-5 (Ger) |
| 417-22 |  |  | 2N1107 |  |  |  |  |  |  |  |  |  |  |  | PNP 16V 5 mA (Ger) |
| 417-23 |  |  | 2N1109 |  |  |  |  |  |  |  |  |  |  |  | PNP 16V 5 mA (Ger) |
| 417-24 |  |  | R-251 |
| 417-25 |  |  | 2N1396 |  |  |  |  |  |  |  |  |  |  |  | PNP 40V 2mA TO-33 (Ger) |
| 417-26 |  |  | 2N1225 |  |  |  |  |  |  |  |  |  |  |  | PNP 40V 10mA TO-12 (Ger) |
| 417-27 |  |  | 2N409 |  |  |  |  |  |  |  |  |  |  |  | PNP 10V 15mA TO-40 (Ger) |
| 417-28 |  |  | 2N407 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 35mA (Ger) |
| 417-29 |  |  | 2N1147 |  |  |  |  |  |  |  |  |  |  |  | PNP 100V 5mA TO-41 (Ger) |
| 417-30 |  |  | CDT1337 |
| 417-31 |  |  | 600RF |
| 417-32 |  |  | 2N383 |  |  |  |  |  |  |  |  |  |  |  | PNP 50V 400mA TO-5 (Ger) |
| 417-33 |  |  | R-424 |
| 417-34 |  |  | 600RFA |
| 417-35 |  |  | TS603 |  |  |  |  |  |  |  |  |  |  |  | PNP 32V 1A TO-3 (Ger) |
| 417-36 |  |  | R-425 |
| 417-37 |  |  | 2N1726 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 50mA TO-9 (Ger) |
| 417-38 |  |  | 2N1727 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 50mA TO-9 (Ger) |
| 417-39 |  |  | 2N1108 Selected |  |  |  |  |  |  |  |  |  |  |  | PNP 16V 5 mA (Ger) |
| 417-40 |  |  | T-6025 |
| 417-41 |  |  | T-6026 |
| 417-42 |  |  | CQT701A |  |  | 2N1548 |  |  |  |  |  | PNP 60V 5A TO-3 (Ger) |
| 417-43 |  |  | 2N398A |  |  |  |  |  |  |  |  |  |  |  | PNP 50V 150mA TO-5 (Ger) |
| 417-44 |  |  | 2N2147 |  |  |  |  |  |  |  |  |  |  |  | PNP 75V 5A TO-3 (Ger) |
| 417-46 |  |  | 34022 |
| 417-47 |  |  | T-1577 |
| 417-50 |  |  | TI363 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 10mA 700MHz (Ger) |
| 417-51 |  |  | 2N185 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 100mA TO-22 (Ger) |
| 417-53 |  |  | TI364 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 10mA 900MHz (Ger) |
| 417-54 |  |  | T2384 |
| 417-56 |  |  | T2379 |
| 417-57 |  |  | 2N1747 |  |  |  |  |  |  |  |  |  |  |  | PNP RF-Amp (Ger) |
| 417-59 |  |  | 2N2217 |  |  |  |  |  |  |  |  |  |  |  | NPN 60V 800mA TO-5 |
| 417-62 |  |  | 34715 |
| 417-66 |  |  | 34942 |
| 417-67 |  |  | 2N2712 |  |  |  |  |  |  |  |  |  |  |  | NPN 18V 100mA TO-98 |
| 417-68 |  |  | 35070 |
| 417-70 |  |  | 2N2671 |  |  |  |  |  |  |  |  |  |  |  | PNP 25V 10mA TO-12 (Ger) |
| 417-71 |  |  | 2N2654 |  |  |  |  |  |  |  |  |  |  |  | PNP 25V 10mA TO-12 (Ger) |
| 417-72 |  |  | 2N2495 |  |  |  |  |  |  |  |  |  |  |  | PNP 40V 10mA TO-12 (Ger) |
| 417-73 |  |  | 2N1525 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 10mA TO-72 (Ger) |
| 417-74 |  |  | 2N1526 |  |  |  |  |  |  |  |  |  |  |  | PNP 24V 10mA TO-1 (Ger) |
| 417-77 |  |  | 2N2712 Selected |  |  |  |  |  |  |  |  |  |  |  | NPN 18V 100mA TO-98 |
| 417-78 |  |  | 2N1524 |  |  |  |  |  |  |  |  |  |  |  | PNP 24V 10mA TO-1 (Ger) |
| 417-82 |  |  | B846 |
| 417-83 |  |  | L842 |  |  | 2N3854 |  |  |  |  |  | NPN 30V 50mA TO-92 |
| 417-84 |  |  | E843 |  |  |  |  |  |  |  |  |  |  |  | NPN 30V 50mA TO-92 |
| 417-85 |  |  | E844 |  |  |  |  |  |  |  |  |  |  |  | NPN 30V 50mA TO-92 |
| 417-86 |  |  | A845 |  |  | 2N2924 |  |  |  |  |  | NPN 30V 500mA TO-92 |
| 417-89 |  |  | 7409 |  |  |  |  |  |  |  |  |  |  |  | 25 V Dual Gate N-ChN MOSFET |
| 417-90 |  |  | 40050 |  |  |  |  |  |  |  |  |  |  |  | PNP 40V 5A TO-3 (Ger) |
| 417-91 |  |  | 2N5232A |  |  |  |  |  |  |  |  |  |  |  | NPN 50V 100mA 0.3W TO-92 |
| 417-93 |  |  | 2N3646 |  |  |  |  |  |  |  |  |  |  |  | NPN 15V 200mA TO-106 (200MHz) |
| 417-94 |  |  | 2N3416 |  |  |  |  |  |  |  |  |  |  |  | NPN 50V 500mA TO-92 |
| 417-96 |  |  | 4JX5E670 |  |  |  |  |  |  |  |  |  |  |  | Unijunction Transistor |
| 417-99 |  |  | 2N2148 |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 10mA TO-18 (300MHz) |
| 417-100 |  |  | 2N3053 |  |  |  |  |  |  |  |  |  |  |  | NPN 60V 700mA 1W TO-39 |
| 417-101 |  |  | TA2577A |  |  |  |  |  |  |  |  |  |  |  | NPN 100V 15A TO-3 |
| 417-103 |  |  | 2N1303 |  |  |  |  |  |  |  |  |  |  |  | PNP 30V 300mA TO-5 (Ger) |
| 417-104 |  |  | 37436 |
| 417-105 |  |  | SE5023 |  |  |  |  |  |  |  |  |  |  |  | NPN 45V 50mA 600MHz |
| 417-106 |  |  | SE5024 |  |  |  |  |  |  |  |  |  |  |  | NPN 45V 50mA 600MHz |
| 417-107 |  |  | SE5025 |  |  |  |  |  |  |  |  |  |  |  | NPN 45V 50mA 600MHz |
| 417-108 |  |  | 2N3692 |  |  |  |  |  |  |  |  |  |  |  | NPN 20V 200mA TO-92 (200MHz) |
| 417-109 |  |  | 2N3566 |  |  |  |  |  |  |  |  |  |  |  | NPN 30V 200mA TO-105 (40MHz) |
| 417-110 |  |  | S2090 |
| 417-112 |  |  | 2N3731 |  |  |  |  |  |  |  |  |  |  |  | PNP 320V 10A TO-3 (Ger) |
| 417-114 |  |  | 2N3567 |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 500mA TO-105 (60MHz) |
| 417-115 |  |  | 2N3923 |  |  |  |  |  |  |  |  |  |  |  | NPN 300V 10mA TO-39 |
| 417-116 |  |  | S2091 |  |  |  |  |  |  |  |  |  |  |  | PNP 80V 1A |
| 417-118 |  |  | 2N3393 |  |  |  |  |  |  |  |  |  |  |  | NPN 25V 0.5A .625W TO-92 |
| 417-119 |  |  | CA3013 |  |  |  |  |  |  |  |  |  |  |  | Transistor Array (TV-Sound) |
| 417-120 |  |  | Unspecified |  |  |  |  |  |  |  |  |  |  |  | PNP Germanium Power Transistor |
| 417-121 |  |  | 2N2430 |  |  |  |  |  |  |  |  |  |  |  | NPN 32V 300mA TO-1 (Ger) |
| 417-122 |  |  | 2N2431 |  |  |  |  |  |  |  |  |  |  |  | PNP 32V 300mA TO-1 (Ger) |
| 417-123 |  |  | CA3012 |  |  |  |  |  |  |  |  |  |  |  | Wide Band IF Amp (Linear IC) |
| 417-125 |  |  | 2N3563 |  |  |  |  |  |  |  |  |  |  |  | NPN 30V 200mA TO-106 (300MHz) |
| 417-126 |  |  | 2N3565 |  |  |  |  |  |  |  |  |  |  |  | NPN 25V 200mA TO-106 |
| 417-133 |  |  | 40245 |  |  |  |  |  |  |  |  |  |  |  | NPN 45V 300mA TO-72 (UHF) |
| 417-134 |  |  | MPS6520 |  |  |  |  |  |  |  |  |  |  |  | NPN 25V 100mA TO-92 (120MHz) |
| 417-135 |  |  | 2N3859A |  |  |  |  |  |  |  |  |  |  |  | NPN 30V 100mA TO-98 (100MHz) |
| 417-136 |  |  | 40408 |  |  |  |  |  |  |  |  |  |  |  | NPN 90V 700mA TO-5 (100MHz) |
| 417-137 |  |  | 40409 |  |  |  |  |  |  |  |  |  |  |  | NPN 90V 700mA TO-5 (100MHz) |
| 417-138 |  |  | 40410 |  |  |  |  |  |  |  |  |  |  |  | PNP 90V 700mA TO-5 (100MHz) |
| 417-139 |  |  | 40411 |  |  |  |  |  |  |  |  |  |  |  | NPN 90V 30A 150W TO-3 |
| 417-140 |  |  | 2N4304 |  |  |  |  |  |  |  |  |  |  |  | JFET 30V 15mA TO-106 (N-Ch) |
| 417-141 |  |  | 2N2869 |  |  | 2N301 |  |  |  |  |  | PNP 50V 10A TO-3 30W (Ger) |
| 417-142 |  |  | DTG-600 |  |  |  |  |  |  |  |  |  |  |  | PNP 50V 15A 60W TO-204 (Ger) |
| 417-144 |  |  | MJE521 |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 4A 40W TO-127 |
| 417-145 |  |  | MJE371 |  |  |  |  |  |  |  |  |  |  |  | PNP 40V 4A 40W TO-126 |
| 417-150 |  |  | 2N1274 |  |  |  |  |  |  |  |  |  |  |  | PNP 25V 50mA TO-5 (Ger) |
| 417-154 |  |  | 2N2369 |  |  | 2N2369A |  |  |  |  |  | NPN 40V 200mA .36W TO-18 |
| 417-155 |  |  | 2N3641 |  |  |  |  |  |  |  |  |  |  |  | NPN 60V 500mA |
| 417-162 |  |  | 2N3055 |  |  | MHT9210 |  |  |  |  |  | NPN 100V 15A 115W TO-3 |
| 417-164 |  |  | 16G2349 |
| 417-167 |  |  | UC734 |  |  |  |  |  |  |  |  |  |  |  | JFET 30V 10mA TO-72 (N-Ch) |
| 417-168 |  |  | TIS37 |  |  |  |  |  |  |  |  |  |  |  | PNP 80V 1A TO-92 |
| 417-169 |  |  | MPF105 |  |  | 2N5459 |  |  |  |  |  | JFET 25V 16mA TO-92 (N-Ch) |
| 417-170 |  |  | MPS6522 |  |  |  |  |  |  |  |  |  |  |  | PNP 25V 100mA TO-92 |
| 417-171 |  |  | 2N3694 |  |  |  |  |  |  |  |  |  |  |  | NPN 45V 30mA TO-106 (200MHz) |
| 417-172 |  |  | MPS6521 |  |  |  |  |  |  |  |  |  |  |  | NPN 25V 100mA TO-92 (120MHz) |
| 417-173 |  |  | ETS083 |  |  | 2N2509 |  |  |  |  |  | NPN 80V 200mA TO-18 |
| 417-174 |  |  | PET9001 |
| 417-175 |  |  | 2N5294 |  |  | TA2911 |  |  |  |  |  | NPN 75V 4A TO-220 (800kHz) |
| 417-178 |  |  | 40389 |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 700mA TO-5 (100MHz) |
| 417-180 |  |  | 40346 |  |  |  |  |  |  |  |  |  |  |  | NPN 175V 1A TO-5 |
| 417-181 |  |  | 40391 |  |  |  |  |  |  |  |  |  |  |  | PNP 60V 1A TO-5 w/HS |
| 417-183 |  |  | 2N4894 |
| 417-186 |  |  | 2N3958 |  |  |  |  |  |  |  |  |  |  |  | JFET 50V 5 mA TO-92 |
| 417-190 |  |  | 40481 |  |  |  |  |  |  |  |  |  |  |  | NPN 45V 50mA TO-72 |
| 417-191 |  |  | TD101 |  |  |  |  |  |  |  |  |  |  |  | NPN 60V 500mA 200MHz |
| 417-195 |  |  | MJE340 |  |  |  |  |  |  |  |  |  |  |  | NPN 300V 500mA 20W TO-225 |
| 417-200 |  |  | X29A826 |  |  |  |  |  |  |  |  |  |  |  | PNP 80V 1A TO-92 |
| 417-201 |  |  | X29A829 |  |  | D29A4 |  | 2N3906 |  | PNP 80V 1A TO-92 |
| 417-203 |  |  | TA7311 |  |  |  |  |  |  |  |  |  |  |  | NPN 70V 10A TO-127 |
| 417-205 |  |  | 2N3866 |  |  |  |  |  |  |  |  |  |  |  | NPN 55V 400mA TO-39 (UHF) |
| 417-206 |  |  | 40673 |  |  | 40675 |  | 3N201 |  | Dual Gate MOS-FET20V 50mA TO72 |
| 417-207 |  |  | 40468 |  |  |  |  |  |  |  |  |  |  |  | MOS-FET 20V 20mA TO-104 (N-Ch) |
| 417-213 |  |  | 2N5249A |  |  |  |  |  |  |  |  |  |  |  | NPN 50V 100mA 0.3W TO-92 |
| 417-215 |  |  | 2N3055 |  |  |  |  |  |  |  |  |  |  |  | NPN 100V 15A 115W TO-3 |
| 417-218 |  |  | TZ1160 |
| 417-219 |  |  | SS9328 |  |  |  |  |  |  |  |  |  |  |  | PNP 180V 1A TO-202 |
| 417-220 |  |  | SS9327 |  |  | MM3006 |  |  |  |  |  | NPN 180V 1A TO-202 |
| 417-221 |  |  | TZ582 |  |  |  |  |  |  |  |  |  |  |  | PNP 60V .5A TO-92 |
| 417-222 |  |  | 2N5308 |  |  |  |  |  |  |  |  |  |  |  | NPN Dar 40V 300mA 0.4W TO-92 |
| 417-223 |  |  | 40673 |  |  | 40675 |  | 3N201 |  | Dual Gate MOS-FET20V 50mA TO72 |
| 417-224 |  |  | MPSU05 |  |  |  |  |  |  |  |  |  |  |  | NPN 60V 2A Mot "Uni-Watt" |
| 417-225 |  |  | MPSU55 |  |  |  |  |  |  |  |  |  |  |  | PNP 60V 2A Mot "Uni-Watt" |
| 417-228 |  |  | SE5055 |  |  |  |  |  |  |  |  |  |  |  | NPN 20V 15mA TO-72 |
| 417-229 |  |  | MPS6544 |  |  |  |  |  |  |  |  |  |  |  | NPN 60V 100mA TO-92 |
| 417-230 |  |  | 40646 |
| 417-232 |  |  | SE7056 |  |  | FT123 |  |  |  |  |  | NPN 300V 30mA TO-39 |
| 417-233 |  |  | 2N3643 |  |  |  |  |  |  |  |  |  |  |  | NPN 30V 500mA TO-105 |
| 417-234 |  |  | 2N3638A |  |  |  |  |  |  |  |  |  |  |  | PNP 25V 500mA TO-92 (100MHz) |
| 417-235 |  |  | 2N4121 |  |  |  |  |  |  |  |  |  |  |  | PNP 40V 200mA TO-106 (UHF) |
| 417-237 |  |  | SE6020 |  |  |  |  |  |  |  |  |  |  |  | NPN 60V 1A TO-105 |
| 417-238 |  |  | 40648 |
| 417-239 |  |  | TA7420 |  |  | MJ3029 |  |  |  |  |  | NPN 800V 10A TO-3 Horiz Output |
| 417-240 |  |  | 40673 |  |  | 40675 |  | 3N201 |  | Dual Gate MOS-FET20V 50mA TO72 |
| 417-241 |  |  | EL131 |  |  |  |  |  |  |  |  |  |  |  | JFET 25V 10mA (N-Ch) |
| 417-242 |  |  | Unspecified |  |  |  |  |  |  |  |  |  |  |  | *Select Zener (Transistor) |
| 417-244 |  |  | 2N5089 |  |  |  |  |  |  |  |  |  |  |  | NPN 25V 50mA 0.3W TO-92 |
| 417-245 |  |  | D40N1 |  |  | MJE340 |  |  |  |  |  | NPN 250V 100mA TO-202 (90MHz) |
| 417-246 |  |  | TIS74 |  |  |  |  |  |  |  |  |  |  |  | JFET 30V 100mA TO-92 |
| 417-251 |  |  | SFC2912 |  |  | UC734 |  |  |  |  |  | JFET |
| 417-254 |  |  | MJ802 |  |  |  |  |  |  |  |  |  |  |  | NPN 90V 30A 200W TO-3 |
| 417-256 |  |  | 2N4360 |  |  | 2N5033 |  |  |  |  |  | FET |
| 417-258 |  |  | TIS87 |  |  |  |  |  |  |  |  |  |  |  | NPN 45V 50mA TO-92 (UHF) |
| 417-260 |  |  | 2N4258A |  |  |  |  |  |  |  |  |  |  |  | PNP 12V 50mA TO-222 (UHF) |
| 417-261 |  |  | TD401 |  |  |  |  |  |  |  |  |  |  |  | PNP 40V .5A |
| 417-263 |  |  | SJE607 |  |  |  |  |  |  |  |  |  |  |  | PNP 80V 4A TO-126 |
| 417-264 |  |  | SJE608 |  |  |  |  |  |  |  |  |  |  |  | NPN 80V 4A TO-126 |
| 417-265 |  |  | 2N5033 |  |  |  |  |  |  |  |  |  |  |  | JFET 20V 3.5mA TO-18 (P-Ch) |
| 417-267 |  |  | MPS6560 |  |  |  |  |  |  |  |  |  |  |  | NPN 25V 500mA TO-92 |
| 417-268 |  |  | MPS6562 |  |  |  |  |  |  |  |  |  |  |  | PNP 80V 1A TO-92 |
| 417-269 |  |  | SGC5282 |
| 417-270 |  |  | SGC5283 |
| 417-272 |  |  | D40C1 |  |  |  |  |  |  |  |  |  |  |  | NPN Dar 30V 500mA TO-202 |
| 417-274 |  |  | 40673 |  |  | 40675 |  | 3N201 |  | Dual Gate MOS-FET20V 50mA TO72 |
| 417-275 |  |  | MPS6522 |  |  |  |  |  |  |  |  |  |  |  | PNP 25V 100mA TO-92 |
| 417-278 |  |  | Unspecified |  |  |  |  |  |  |  |  |  |  |  | PNP Germanium Power (Selected) |
| 417-279 |  |  | FM1108 |  |  |  |  |  |  |  |  |  |  |  | Dual FET |
| 417-282 |  |  | MJ2841 |  |  |  |  |  |  |  |  |  |  |  | NPN 80V 10A 150W TO-3 |
| 417-283 |  |  | SMO7275 |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 800mA 300MHz |
| 417-284 |  |  | SM62186 |  |  |  |  |  |  |  |  |  |  |  | PNP 15V 200mA 850MHz |
| 417-286 |  |  | 2N4347 |  |  |  |  |  |  |  |  |  |  |  | NPN 250V 15A TO-3 |
| 417-288 |  |  | 2N4416 |  |  | PN4416 |  |  |  |  |  | JFET 30V 30mA TO-72 (N-Ch) |
| 417-289 |  |  | 2N6109 |  |  |  |  |  |  |  |  |  |  |  | PNP 50V 7A TO-220 (10MHz) |
| 417-290 |  |  | MRF502 |  |  |  |  |  |  |  |  |  |  |  | NPN 35V 50mA TO-72 (UHF) |
| 417-291 |  |  | 2N5458 |  |  |  |  |  |  |  |  |  |  |  | JFET 25V 0.25A TO-92 (N-Ch) |
| 417-292 |  |  | 2N5771 |  |  |  |  |  |  |  |  |  |  |  | PNP 30V 0.05A 0.63W TO-92 |
| 417-293 |  |  | 2N5770 |  |  |  |  |  |  |  |  |  |  |  | NPN 30V 0.05A 0.63W TO-92 |
| 417-294 |  |  | MPSA42 |  |  |  |  |  |  |  |  |  |  |  | NPN 300V 500mA TO-92 (50MHz) |
| 417-295 |  |  | MPSL51 |  |  | 2N5400 |  | 2N5401 |  | PNP 100V 600mA TO-92 |
| 417-296 |  |  | TA311 |
| 417-298 |  |  | TIP41B |  |  |  |  |  |  |  |  |  |  |  | NPN 80V 300mA TO-220 |
| 417-299 |  |  | 2N5591 |  |  | CTC B25-12 |  |  |  |  |  | NPN 36V 4.0A 200MHz T72 |
| 417-801 |  |  | MPSA20 |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 100mA TO-92 (125MHz) |
| 417-802 |  |  | E304 |  |  | MPF102 (Selected) |  |  |  |  |  | JFET 30V 15mA (N-Ch) |
| 417-803 |  |  | 2N6081 |  |  | 2N5590 |  |  |  |  |  | NPN 18V 2.5A 30W Stx-8 |
| 417-804 |  |  | 2N6080 |  |  | 2N5589 |  |  |  |  |  | NPN 18V 1A 12W Stx-8 |
| 417-805 |  |  | 2N4889 |  |  |  |  |  |  |  |  |  |  |  | PNP 150V 100mA TO-222 (160MHz) |
| 417-806 |  |  | TIS75 |  |  |  |  |  |  |  |  |  |  |  | JFET 30V 10mA TO-92 (N-Ch) |
| 417-807 |  |  | 2N6175 |  |  |  |  |  |  |  |  |  |  |  | NPN 250V 1A TO-126 (20MHz) |
| 417-808 |  |  | 2N3702 |  |  |  |  |  |  |  |  |  |  |  | PNP 25V 0.5A .625WTO-92 |
| 417-809 |  |  | 2N3704 |  |  |  |  |  |  |  |  |  |  |  | NPN 50V 800mA TO-92 |
| 417-811 |  |  | MPSL01 |  |  | 2N5550 |  | 2N5551 |  | NPN 120V 150mA TO-92 |
| 417-812 |  |  | E421 |  |  |  |  |  |  |  |  |  |  |  | Dual JFET 50V 50mA (N-Ch) |
| 417-813 |  |  | 2N4959 |  |  |  |  |  |  |  |  |  |  |  | PNP 30V 200mA TO-72 (450MHz) |
| 417-814 |  |  | DTS409 |  |  |  |  |  |  |  |  |  |  |  | NPN 400V 3.5A TO-3 |
| 417-818 |  |  | MJE181 |  |  |  |  |  |  |  |  |  |  |  | NPN 60V 3A 12W TO-225 |
| 417-819 |  |  | MJE171 |  |  |  |  |  |  |  |  |  |  |  | PNP 60V 3A 12W TO-225 |
| 417-820 |  |  | 2N4342 |  |  |  |  |  |  |  |  |  |  |  | JFET 25V 12mA TO-222 (P-Ch) |
| 417-821 |  |  | MPSA06 |  |  |  |  |  |  |  |  |  |  |  | NPN 80V 500mA TO-92 (100MHz) |
| 417-822 |  |  | MPSA56 |  |  |  |  |  |  |  |  |  |  |  | PNP 80V 500mA TO-92 (50MHz) |
| 417-823 |  |  | MPU131 |  |  |  |  |  |  |  |  |  |  |  | Uni-Junction 40V 200mA TO-92 |
| 417-828 |  |  | E304 (Selected) |  |  | MPF102 (Selected) |  |  |  |  |  | JFET 30V 15mA (N-Ch) Idss=10 |
| 417-830 |  |  | PT6619 |  |  | CD3342 |
| 417-831 |  |  | 2N6456 |  |  | CD2664A |  | PT5767 |  | NPN 25V 12A 75W (60MHz) |
| 417-833 |  |  | 2N6306 |  |  |  |  |  |  |  |  |  |  |  | NPN 250V 8A TO-3 (5MHz) |
| 417-834 |  |  | MPSU10 |  |  |  |  |  |  |  |  |  |  |  | NPN 300V 500mA Mot "Uni-Watt" |
| 417-836 |  |  | MPSD51 |  |  |  |  |  |  |  |  |  |  |  | PNP 200V 100mA TO-92 |
| 417-839 |  |  | 2N5179 |  |  |  |  |  |  |  |  |  |  |  | NPN 20V 50mA TO-72 (UHF) |
| 417-847 |  |  | 1B05 |  |  |  |  |  |  |  |  |  |  |  | NPN 250V TO-3 |
| 417-849 |  |  | TZ553 |  |  |  |  |  |  |  |  |  |  |  | PNP 60V .5A TO-92 |
| 417-851 |  |  | LPT1000 |  |  |  |  |  |  |  |  |  |  |  | Photo Diode |
| 417-852 |  |  | TIP31B |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 3A TO-220 |
| 417-853 |  |  | SF83045 |
| 417-854 |  |  | SF50077 |  |  | E304 |  |  |  |  |  | JFET 30V 15mA (N-Ch) |
| 417-856 |  |  | MJE5979 |  |  |  |  |  |  |  |  |  |  |  | NPN 100V 5A 75W TO-220 |
| 417-857 |  |  | MJE5976 |  |  |  |  |  |  |  |  |  |  |  | PNP 60V 10A 90W TO-127 |
| 417-858 |  |  | P1087E |  |  |  |  |  |  |  |  |  |  |  | JFET 30V 5mA TO-92 (P-Ch) |
| 417-863 |  |  | MFE131 |  |  |  |  |  |  |  |  |  |  |  | Dual Gate MOS-FET25V 30mA TO72 |
| 417-864 |  |  | MPSA05 |  |  |  |  |  |  |  |  |  |  |  | NPN 60V 500mA TO-92 (100MHz) |
| 417-865 |  |  | MPSA55 |  |  |  |  |  |  |  |  |  |  |  | PNP 60V 500mA TO-92 (50MHz) |
| 417-868 |  |  | RCA29C |  |  |  |  |  |  |  |  |  |  |  | NPN 100V 3A TO-220 |
| 417-869 |  |  | RCA30C |  |  |  |  |  |  |  |  |  |  |  | PNP 100V 3A TO-220 |
| 417-870 |  |  | RCA1A16 |  |  |  |  |  |  |  |  |  |  |  | PNP 100V 1A TO-39 |
| 417-872 |  |  | TIP32 |  |  |  |  |  |  |  |  |  |  |  | PNP 70V 7A TO-220 |
| 417-874 |  |  | 2N3906 |  |  |  |  |  |  |  |  |  |  |  | PNP 40V 0.2A 310mW TO-92 |
| 417-875 |  |  | 2N3904 |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 0.2A 310mW TO-92 |
| 417-876 |  |  | CA3046 |  |  |  |  |  |  |  |  |  |  |  | Transistor Array Diff Amp (3) |
| 417-877 |  |  | CA3018A |  |  |  |  |  |  |  |  |  |  |  | Transistor Array Darlington |
| 417-878 |  |  | Selected FET |
| 417-879 |  |  | 2N3251 |  |  |  |  |  |  |  |  |  |  |  | PNP 40V 200mA TO-18 (300MHz) |
| 417-880 |  |  | 2N4427 |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 400mA TO-39 (UHF) |
| 417-881 |  |  | MPSA13 |  |  |  |  |  |  |  |  |  |  |  | NPN Darl 30V 500mA TO-92 |
| 417-882 |  |  | MPSA20 (Selected) |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 100mA TO-92 (125MHz) |
| 417-883 |  |  | MPSU10 (Selected) |  |  |  |  |  |  |  |  |  |  |  | NPN 300V 500mA Mot "Uni-Watt" |
| 417-884 |  |  | Unspecified |  |  |  |  |  |  |  |  |  |  |  | Selected Transistor (Zener) |
| 417-885 |  |  | MPSA65 |  |  |  |  |  |  |  |  |  |  |  | PNP Darl 30V 300mA TO-92 |
| 417-887 |  |  | MPSH10 |  |  |  |  |  |  |  |  |  |  |  | NPN 30V 40mA TO-92 (UHF) |
| 417-892 |  |  | MJ2941 |  |  |  |  |  |  |  |  |  |  |  | NPN 80V 10A 150W TO-3 |
| 417-893 |  |  | 2N5109 |  |  |  |  |  |  |  |  |  |  |  | NPN 35V 500mA TO-39 (UHF) |
| 417-895 |  |  | PIC625 |
| 417-896 |  |  | PIC600 |
| 417-897 |  |  | Selected FET |
| 417-900 |  |  | S2090 Selected |
| 417-901 |  |  | S2091 Selected |  |  |  |  |  |  |  |  |  |  |  | PNP 80V 1A |
| 417-902 |  |  | NPD5566N |  |  |  |  |  |  |  |  |  |  |  | JFET 40V 30mA N-Ch Dual 8-PDIP |
| 417-903 |  |  | 40363 |  |  |  |  |  |  |  |  |  |  |  | NPN 35V 7A TO-3 |
| 417-904 |  |  | MPSU60 |  |  |  |  |  |  |  |  |  |  |  | PNP 300V 500mA TO-92 |
| 417-905 |  |  | 2N3773 |  |  |  |  |  |  |  |  |  |  |  | NPN 140V 16A TO-3 (200kHz) |
| 417-906 |  |  | 2N6609 |  |  |  |  |  |  |  |  |  |  |  | PNP 140V 16A 150W TO-3 200MHz |
| 417-907 |  |  | 2N6274 |  |  |  |  |  |  |  |  |  |  |  | PNP 100V 50mA TO-3 |
| 417-908 |  |  | 2N4117 |  |  |  |  |  |  |  |  |  |  |  | JFET 40V 50mA TO-72 (N-Ch) |
| 417-912 |  |  | MRF237 |  |  |  |  |  |  |  |  |  |  |  | NPN 18V 1A TO-39 (UHF) |
| 417-914 |  |  | F-317-B |  |  |  |  |  |  |  |  |  |  |  | NPN 140V 2A TO-220 |
| 417-915 |  |  | F-417-B |  |  |  |  |  |  |  |  |  |  |  | PNP 140V 2A TO-220 |
| 417-917 |  |  | MPSH81 |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 40mA TO-92 (UHF) |
| 417-918 |  |  | 2N6387 |  |  |  |  |  |  |  |  |  |  |  | NPN Dar 60V 10A TO-220 (20MHz) |
| 417-919 |  |  | TIL78 |  |  | QSC114 |  |  |  |  |  | Photo Transistor T1 |
| 417-920 |  |  | 2N4403 |  |  |  |  |  |  |  |  |  |  |  | PNP 40V 600mA 0.3W TO-92 |
| 417-923 |  |  | BU-500 |  |  |  |  |  |  |  |  |  |  |  | NPN 1500V 6A TO-3 |
| 417-924 |  |  | MJE172 |  |  |  |  |  |  |  |  |  |  |  | PNP 100V 3A 12W TO-225 |
| 417-926 |  |  | MPSU06 |  |  |  |  |  |  |  |  |  |  |  | NPN 80V 2A Mot "Uni-Watt" |
| 417-927 |  |  | MPSA93 |  |  |  |  |  |  |  |  |  |  |  | PNP 200V 500mA TO-92 |
| 417-928 |  |  | 2N6592 |  |  |  |  |  |  |  |  |  |  |  | NPN 200V .5A TO-220 (70MHz) |
| 417-931 |  |  | PN4858 |  |  |  |  |  |  |  |  |  |  |  | JFET 40V 50mA TO-92 (N-Ch) |
| 417-932 |  |  | MJE182 |  |  |  |  |  |  |  |  |  |  |  | NPN 100V 3A 12W TO-225 |
| 417-934 |  |  | 2N5770 (Selected) |  |  |  |  |  |  |  |  |  |  |  | NPN 30V 0.05A 0.63W TO-92 |
| 417-937 |  |  | MPS2369 |  |  |  |  |  |  |  |  |  |  |  | NPN 40V 500mA TO-92 (UHF) |
| 417-943 |  |  | MJE15030 |  |  |  |  |  |  |  |  |  |  |  | NPN 150V 8A TO-220 |
| 417-944 |  |  | MJE15031 |  |  |  |  |  |  |  |  |  |  |  | PNP 150V 8A TO-220 |
| 417-945 |  |  | MJ15024 |  |  |  |  |  |  |  |  |  |  |  | NPN 250V 16A TO-3 |
| 417-946 |  |  | MJ15025 |  |  |  |  |  |  |  |  |  |  |  | PNP 250V 16A TO-3 |
| 417-947 |  |  | MDS21 |  |  |  |  |  |  |  |  |  |  |  | NPN 300V 500mA TO-202 |
| 417-948 |  |  | MDS60 |  |  |  |  |  |  |  |  |  |  |  | PNP 300V 500mA TO-202 |
| 417-951 |  |  | MRF247 |  |  |  |  |  |  |  |  |  |  |  | NPN 35V 20A 6-Tab 175MHz |
| 417-952 |  |  | 2N6081 |  |  |  |  |  |  |  |  |  |  |  | NPN 18V 2.5A 30W Stx-8 |
| 417-953 |  |  | TIP150 |  |  |  |  |  |  |  |  |  |  |  | NPN 300V 7A TO-220 |
| 417-959 |  |  | MD5000B |  |  |  |  |  |  |  |  |  |  |  | PNP 20V 50mA TO-99 |
| 417-962 |  |  | MRF421 |  |  |  |  |  |  |  |  |  |  |  | NPN 20V 20A 290W (UHF) |
| 417-965 |  |  | NSDU06 |  |  |  |  |  |  |  |  |  |  |  | NPN 80V 2A "Uni-Watt 50MHz |
| 417-975 |  |  | CA3127 |  |  |  |  |  |  |  |  |  |  |  | NPN Transistor Array Ind |
| 417-999 |  |  | VN10KM |  |  |  |  |  |  |  |  |  |  |  | JFET 60V .5A TO-92TAB |
| Linear IC |
| 442-2 |  |  | SN4985N |  |  | SN82809 |
| 442-3 |  |  | SN72710 |  |  | LM710 |  |  |  |  |  | Voltage Comparator |
| 442-4 |  |  | CA3035 |  |  |  |  |  |  |  |  |  |  |  | RF Amp IC |
| 442-5 |  |  | CA3044VI |
| 442-9 |  |  | MC1310P |  |  |  |  |  |  |  |  |  |  |  | MPX Decoder |
| 442-10 |  |  | uA746E |  |  |  |  |  |  |  |  |  |  |  | Dual Chroma Demodulator |
| 442-11 |  |  | CA3042 |
| 442-18 |  |  | MC1350P |  |  |  |  |  |  |  |  |  |  |  | Video IF Amp IC |
| 442-19 |  |  | 75450N |  |  |  |  |  |  |  |  |  |  |  | Dual Peripheral Driver |
| 442-20 |  |  | uA703 |  |  |  |  |  |  |  |  |  |  |  | Op Amp |
| 442-21 |  |  | MC1458 |  |  |  |  |  |  |  |  |  |  |  | Dual 741C |
| 442-22 |  |  | N5741V |  |  |  |  |  |  |  |  |  |  |  | Op Amp |
| 442-24 |  |  | LM376 |  |  |  |  |  |  |  |  |  |  |  | Adj Voltage Regulator (Pos) |
| 442-25 |  |  | LM310H |  |  |  |  |  |  |  |  |  |  |  | Op Amp Follower |
| 442-28 |  |  | MC1357P |  |  |  |  |  |  |  |  |  |  |  | IF Amp Quadrature Detector |
| 442-30 |  |  | uA309K |  |  |  |  |  |  |  |  |  |  |  | 5 V Regulator (Pos) |
| 442-33 |  |  | MC1328 |
| 442-34 |  |  | 87403 |  |  |  |  |  |  |  |  |  |  |  | Four Channel Decoder Chip |
| 442-35 |  |  | uA308AHC |  |  |  |  |  |  |  |  |  |  |  | Precision Op Amp |
| 442-36 |  |  | LM311 |  |  |  |  |  |  |  |  |  |  |  | Comparitor |
| 442-39 |  |  | LM301A |  |  | LM101 |  |  |  |  |  | Op Amp |
| 442-41 |  |  | uA739 |  |  |  |  |  |  |  |  |  |  |  | Dual Audio Pre-Amp |
| 442-46 |  |  | MC1310 |  |  |  |  |  |  |  |  |  |  |  | Stereo Decoder PLL |
| 442-47 |  |  | SG-2501 |  |  |  |  |  |  |  |  |  |  |  | Dual Tracking +/- Regulator |
| 442-48 |  |  | MFC6030 |  |  |  |  |  |  |  |  |  |  |  | Regulator IC |
| 442-50 |  |  | U760 |  |  |  |  |  |  |  |  |  |  |  | High Speed Op Amp |
| 442-53 |  |  | NE555V |  |  |  |  |  |  |  |  |  |  |  | General Purpose Timer |
| 442-54 |  |  | uA7805 |  |  |  |  |  |  |  |  |  |  |  | 5 V Regulator (Pos) |
| 442-55 |  |  | MC1349P |  |  |  |  |  |  |  |  |  |  |  | FM / TV Sound IF |
| 442-56 |  |  | MC1330P |  |  |  |  |  |  |  |  |  |  |  | Video Sync Detector |
| 442-57 |  |  | MC1370P |  |  |  |  |  |  |  |  |  |  |  | Sync Detector Sound Demod |
| 442-58 |  |  | MC1371P |  |  |  |  |  |  |  |  |  |  |  | TV Chroma IF Amp |
| 442-59 |  |  | MC1364P |  |  |  |  |  |  |  |  |  |  |  | Automatic Fine Tuning Detector |
| 442-60 |  |  | MC7824 |  |  |  |  |  |  |  |  |  |  |  | 24 V Regulator (Pos) |
| 442-62 |  |  | MC1358P |  |  |  |  |  |  |  |  |  |  |  | TV Sound IF Detector |
| 442-63 |  |  | uA7815 |  |  |  |  |  |  |  |  |  |  |  | 15 V Regulator (Pos) |
| 442-65 |  |  | SG4501N |  |  |  |  |  |  |  |  |  |  |  | Dual Tracking +/- Regulator |
| 442-66 |  |  | LM308 |  |  |  |  |  |  |  |  |  |  |  | Precision Op Amp |
| 442-69 |  |  | MC1312P |  |  |  |  |  |  |  |  |  |  |  | SQ Decoder (4-ch) SQ |
| 442-71 |  |  | LM3900 |  |  |  |  |  |  |  |  |  |  |  | Quad Op Amp |
| 442-73 |  |  | 75107 |  |  |  |  |  |  |  |  |  |  |  | TriState Line Receiver |
| 442-74 |  |  | MD1344P |
| 442-75 |  |  | LM311 |  |  |  |  |  |  |  |  |  |  |  | Comparitor |
| 442-78 |  |  | UHP481 |
| 442-80 |  |  | MC1398P |  |  |  |  |  |  |  |  |  |  |  | TV Color Processor |
| 442-82 |  |  | N5741 |  |  |  |  |  |  |  |  |  |  |  | Op Amp |
| 442-83 |  |  | UHP480 |
| 442-88 |  |  | MC1314P |  |  |  |  |  |  |  |  |  |  |  | Audio Logic (4-ch) SQ |
| 442-89 |  |  | MC1315P |  |  |  |  |  |  |  |  |  |  |  | VCA (4-ch) SQ |
| 442-92 |  |  | CA3089 |  |  |  |  |  |  |  |  |  |  |  | RCA FM IF IC |
| 442-96 |  |  | MC1496G |  |  |  |  |  |  |  |  |  |  |  | Balanced Mod/Demod IC |
| 442-99 |  |  | CD4016 |  |  |  |  |  |  |  |  |  |  |  | CMOS Analog Switch |
| 442-602 |  |  | LM324N |  |  |  |  |  |  |  |  |  |  |  | Quad Op Amp Single Supply |
| 442-603 |  |  | 78M05 |  |  |  |  |  |  |  |  |  |  |  | 5 V Regulator (Pos) |
| 442-604 |  |  | CD4007 |  |  |  |  |  |  |  |  |  |  |  | CMOS Buffer |
| 442-605 |  |  | QSI5022 |  |  |  |  |  |  |  |  |  |  |  | CD-4 Demodulator IC |
| 442-609 |  |  | 78M20C |  |  |  |  |  |  |  |  |  |  |  | 20 V Regulator (Pos) |
| 442-610 |  |  | TBA820 |  |  |  |  |  |  |  |  |  |  |  | Audio Amplifier 2W |
| 442-612 |  |  | LM386N |  |  |  |  |  |  |  |  |  |  |  | 1.5 W Audio Power Amp |
| 442-613 |  |  | MC7915 |  |  |  |  |  |  |  |  |  |  |  | 12 V Regulator (Neg) |
| 442-615 |  |  | uA739 |  |  |  |  |  |  |  |  |  |  |  | Dual Audio Pre-Amp |
| 442-616 |  |  | LM2901 |  |  | uA775 |  | LM3302N |  | Quad Single Supply Comparitor |
| 442-617 |  |  | uA78MGT2C |  |  |  |  |  |  |  |  |  |  |  | Adj Voltage Regulator (Pos) |
| 442-618 |  |  | uA79MGT2C |  |  |  |  |  |  |  |  |  |  |  | Adj Voltage Regulator (Neg) |
| 442-619 |  |  | ICL8049 |  |  |  |  |  |  |  |  |  |  |  | Anti-Log Op Amp |
| 442-620 |  |  | MC1391P |  |  |  |  |  |  |  |  |  |  |  | TV Horizontal Processor |
| 442-621 |  |  | 78M24C |  |  |  |  |  |  |  |  |  |  |  | 24 V Regulator (Pos) |
| 442-622 |  |  | MC1331P |
| 442-623 |  |  | CA3130S |  |  |  |  |  |  |  |  |  |  |  | Op Amp |
| 442-624 |  |  | 5322 |  |  |  |  |  |  |  |  |  |  |  | Color Generator Chip |
| 442-625 |  |  | ULN2111 |  |  |  |  |  |  |  |  |  |  |  | FM IF & Detector IC |
| 442-626 |  |  | 78MGT4C |  |  |  |  |  |  |  |  |  |  |  | Adj Voltage Requlator (Pos) |
| 442-627 |  |  | 78L05 |  |  |  |  |  |  |  |  |  |  |  | 5 V Regulator (Pos) |
| 442-628 |  |  | GPD401 |  |  |  |  |  |  |  |  |  |  |  | Avantek RF Amplifier |
| 442-629 |  |  | GPD402 |  |  |  |  |  |  |  |  |  |  |  | Avantek RF Amplifier |
| 442-630 |  |  | MC7905 |  |  |  |  |  |  |  |  |  |  |  | 5 V Regulator (Neg) |
| 442-638 |  |  | MK5086N-4 |
| 442-639 |  |  | LM308AN |  |  |  |  |  |  |  |  |  |  |  | Op Amp |
| 442-640 |  |  | CA3080 |  |  |  |  |  |  |  |  |  |  |  | High Perf Op Amp |
| 442-644 |  |  | LM78L12 |  |  |  |  |  |  |  |  |  |  |  | 12 V Regulator (Pos) |
| 442-646 |  |  | MC79L12AC |  |  |  |  |  |  |  |  |  |  |  | 12 V Regulator (Neg) |
| 442-647 |  |  | CD4046AE |  |  |  |  |  |  |  |  |  |  |  | CMOS PLL |
| 442-648 |  |  | LM310N |  |  |  |  |  |  |  |  |  |  |  | Op Amp Follower |
| 442-649 |  |  | SF7-0890 |  |  |  |  |  |  |  |  |  |  |  | Avantek RF Amplifier |
| 442-650 |  |  | 78H12 |  |  |  |  |  |  |  |  |  |  |  | 12 V Regulator (Pos) |
| 442-651 |  |  | 78H05 |  |  |  |  |  |  |  |  |  |  |  | 5 V Regulator (Pos) |
| 442-654 |  |  | 565 |  |  |  |  |  |  |  |  |  |  |  | PLL |
| 442-655 |  |  | LM349 |  |  |  |  |  |  |  |  |  |  |  | Quad Wide-band 741 Op Amp |
| 442-658 |  |  | HA1197 |  |  |  |  |  |  |  |  |  |  |  | Signal Meter Drive (Hitachi) |
| 442-663 |  |  | CA3130-05 |  |  |  |  |  |  |  | Heathkit P/N Error |  | Transistor Array |
| 442-663 |  |  | 78M12CKC |  |  |  |  |  |  |  | Heathkit P/N Error |  | 12 V Regulator (Pos) |
| 442-664 |  |  | 79M12CKC |  |  |  |  |  |  |  |  |  |  |  | 12 V Regulator (Neg) |
| 442-665 |  |  | 79L05 |  |  |  |  |  |  |  |  |  |  |  | 5 V Regulator (Neg) |
| 442-670 |  |  | LF356N |  |  |  |  |  |  |  |  |  |  |  | Bi FET Op Amp |
| 442-672 |  |  | NE645B |  |  |  |  |  |  |  |  |  |  |  | Compander Amp |
| 442-674 |  |  | MC7812 |  |  |  |  |  |  |  |  |  |  |  | 12 V Regulator (Pos) |
| 442-675 |  |  | MC7912 |  |  |  |  |  |  |  |  |  |  |  | 12 V Regulator (Neg) |
| 442-676 |  |  | TDA2190 |
| 442-678 |  |  | 7106 |  |  |  |  |  |  |  |  |  |  |  | DVM Chip |
| 442-679 |  |  | TL061CP |  |  |  |  |  |  |  |  |  |  |  | Low Power JFET Op Amp |
| 442-681 |  |  | 78L08 |  |  |  |  |  |  |  |  |  |  |  | 5 V Regulator (Pos) |
| 442-685 |  |  | uA78GKC |  |  |  |  |  |  |  |  |  |  |  | Adj Volt Reg (Pos) TO-3 (4pin) |
| 442-687 |  |  | 78L10 |  |  |  |  |  |  |  |  |  |  |  | 10 V Regulator (Pos) |
| 442-688 |  |  | NE567N |  |  |  |  |  |  |  |  |  |  |  | DTMF Tone Decoder |
| 442-691 |  |  | 78M08 |  |  |  |  |  |  |  |  |  |  |  | 8 V Regulator (Pos) |
| 442-693 |  |  | LM322N |  |  |  |  |  |  |  |  |  |  |  | Precision Timer |
| 442-694 |  |  | uA2240PC |  |  |  |  |  |  |  |  |  |  |  | Programmable Timer |
| 442-695 |  |  | 78L15 |  |  |  |  |  |  |  |  |  |  |  | 15 V Regulator (Pos) |
| 442-696 |  |  | 79L15 |  |  |  |  |  |  |  |  |  |  |  | 15 V Regulator (Neg) |
| 442-698 |  |  | SL952 |  |  |  |  |  |  |  |  |  |  |  | Wide RF Amplifier (512 MHz) |
| 442-699 |  |  | 1873 |  |  | 136PC |  | 137PC15A212 |  | Pressure Transducer (ID-4001) |
| 442-700 |  |  | LM3524 |  |  | SG3524 |  |  |  |  |  | Switching Regulator |
| 442-701 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Pressure Transducer (ID-4001) |
| 442-703 |  |  | LM350K |  |  |  |  |  |  |  |  |  |  |  | Adj Voltage Regulator (Pos) |
| 442-706 |  |  | NE5534 |  |  |  |  |  |  |  |  |  |  |  | Single Low Noise Op Amp |
| 442-707 |  |  | LF353 |  |  |  |  |  |  |  |  |  |  |  | Quad JFET Op Amp |
| 442-708 |  |  | LM317 |  |  |  |  |  |  |  |  |  |  |  | Adj Voltage Regulator (Pos) |
| 442-709 |  |  | LM337 |  |  |  |  |  |  |  |  |  |  |  | Adj Voltage Regulator (Neg) |
| 442-710 |  |  | XR2206 |  |  |  |  |  |  |  |  |  |  |  | VCO IC |
| 442-711 |  |  | LM342 |  |  |  |  |  |  |  |  |  |  |  | Prec Fahrenheit Temp Sensor |
| 442-712 |  |  | LM320 |  |  |  |  |  |  |  |  |  |  |  | Fixed Voltage Regulator |
| 442-715 |  |  | CA3130 |  |  |  |  |  |  |  |  |  |  |  | Op Amp |
| 442-716 |  |  | LM330T |  |  |  |  |  |  |  |  |  |  |  | 5 V Regulator (Pos) |
| 442-721 |  |  | HA12412 |  |  |  |  |  |  |  |  |  |  |  | FM Receiver Chip |
| 442-722 |  |  | uPC1173C |  |  |  |  |  |  |  |  |  |  |  | FM Stereo Decoder |
| 442-723 |  |  | TL489 |  |  |  |  |  |  |  |  |  |  |  | Bar Graph Display |
| 442-724 |  |  | 7107 |  |  |  |  |  |  |  |  |  |  |  | DVM Chip |
| 442-726 |  |  | TL062CP |  |  |  |  |  |  |  |  |  |  |  | Dual JFET Op Amp |
| 442-728 |  |  | LM2904 |  |  |  |  |  |  |  |  |  |  |  | Low Power Op Amp |
| 442-733 |  |  | LM358 |  |  |  |  |  |  |  |  |  |  |  | Dual Op Amp |
| 442-734 |  |  | LM388N |  |  |  |  |  |  |  |  |  |  |  | 1.5 W Audio Power Amp |
| 442-740 |  |  | LM556 |  |  |  |  |  |  |  |  |  |  |  | Dual 555 Timer |
| 442-741 |  |  | XR2209 |  |  |  |  |  |  |  |  |  |  |  | Precision Oscillator (Exar) |
| 442-743 |  |  | HA4741-5 |  |  |  |  |  |  |  |  |  |  |  | Op Amp |
| 442-744 |  |  | CD4066BCN |  |  |  |  |  |  |  |  |  |  |  | Quad Bilateral Switch |
| 442-748 |  |  | ULN2280B |  |  |  |  |  |  |  |  |  |  |  | Audio Power Amp |
| 442-751 |  |  | LM1408N-8 |  |  | DAC0808 |  |  |  |  |  | A/D Converter |
| 442-753 |  |  | 9402 |  |  |  |  |  |  |  |  |  |  |  | V to F Converter |
| 442-756 |  |  | LF347 |  |  | TL074 |  |  |  |  |  | Quad JFET Op Amp |
| 442-759 |  |  | LF411 |  |  |  |  |  |  |  |  |  |  |  | J-FET Op Amp Low Offset |
| 442-760 |  |  | 5437 |  |  |  |  |  |  |  |  |  |  |  | White Noise Generator |
| 442-762 |  |  | LM388N-1 |  |  |  |  |  |  |  |  |  |  |  | 1.5 W Audio Power Amp |
| 442-763 |  |  | LM388N-3 |  |  |  |  |  |  |  |  |  |  |  | 1.5 W Audio Power Amp |
| 442-765 |  |  | TL852CN |  |  |  |  |  |  |  |  |  |  |  | Polaroid Sonar Ranging Reciver |
| 442-768 |  |  | DAC1021 |  |  |  |  |  |  |  |  |  |  |  | 10-Bit (Mult) D/A Converter |
| 442-769 |  |  | ADC0820 |  |  |  |  |  |  |  |  |  |  |  | 8-Bit A/D Converter |
| 442-771 |  |  | LM361 |  |  |  |  |  |  |  |  |  |  |  | High Speed Comparitor |
| 442-774 |  |  | CD4052 |  |  |  |  |  |  |  |  |  |  |  | 4 Chan Analog Mux |
| 442-779 |  |  | MF-10 |  |  |  |  |  |  |  |  |  |  |  | Maxim Switched Cap Act Filter |
| 442-780 |  |  | 2211 |  |  |  |  |  |  |  |  |  |  |  | PLL IC |
| 442-782 |  |  | LF357 |  |  |  |  |  |  |  |  |  |  |  | J-FET Op Amp |
| 442-786 |  |  | MPX100AP |  |  | MPX2100AP |  |  |  |  |  | Presure Transducer (ID-5001) |
| 442-787 |  |  | LP2950C |  |  |  |  |  |  |  |  |  |  |  | Low Drop-out Voltage Regulator |
| 442-789 |  |  | RCA4192 |
| 442-801 |  |  | TLC555 |  |  |  |  |  |  |  |  |  |  |  | CMOS Timer |
| 442-840 |  |  | NE566N |  |  |  |  |  |  |  |  |  |  |  | VCO Function Generator |
| Digital IC |
| 443-1 |  |  | 7400N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-input NAND |
| 443-2 |  |  | 7420N |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Input NAND |
| 443-3 |  |  | 7430N |  |  |  |  |  |  |  |  |  |  |  | 8-Input NAND |
| 443-4 |  |  | 7472N |  |  |  |  |  |  |  |  |  |  |  | JK Flip-Flop |
| 443-5 |  |  | 7473N |  |  |  |  |  |  |  |  |  |  |  | Dual JK Flip-Flop |
| 443-6 |  |  | 7474N |  |  |  |  |  |  |  |  |  |  |  | Dual D Flip-Flop |
| 443-7 |  |  | 7490N |  |  |  |  |  |  |  |  |  |  |  | Decade Counter |
| 443-8 |  |  | MC724P |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NAND (RTL) |
| 443-9 |  |  | MC790P |  |  |  |  |  |  |  |  |  |  |  | Dual J-K FF (RTL) |
| 443-10 |  |  | MC723P |  |  |  |  |  |  |  |  |  |  |  | Single J-K FF (RTL) |
| 443-12 |  |  | 7410N |  |  |  |  |  |  |  |  |  |  |  | Triple 3-Input NAND |
| 443-13 |  |  | 7475N |  |  |  |  |  |  |  |  |  |  |  | 4-Bit Bistable Latch |
| 443-14 |  |  | MC789P (Selected) |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter |
| 443-15 |  |  | 7450N |  |  |  |  |  |  |  |  |  |  |  | Dual 2-Wide 2-In And-OR-Invert |
| 443-16 |  |  | 7476N |  |  |  |  |  |  |  |  |  |  |  | Dual JK Flip-Flop |
| 443-17 |  |  | 74141A |  |  |  |  |  |  |  |  |  |  |  | BCD to Decimal Decoder |
| 443-18 |  |  | 7404N |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter |
| 443-19 |  |  | N8290A |  |  |  |  |  |  |  |  |  |  |  | Decade Counter |
| 443-21 |  |  | MC717P |
| 443-22 |  |  | 74121N |  |  |  |  |  |  |  |  |  |  |  | Monostable Non-Retrig |
| 443-23 |  |  | 74122N |  |  |  |  |  |  |  |  |  |  |  | Retrig Monostable |
| 443-25 |  |  | 74151N |  |  |  |  |  |  |  |  |  |  |  | 8:1 Multiplexer |
| 443-26 |  |  | 74S00 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NAND |
| 443-27 |  |  | SN158093N |  |  | MC668P |  |  |  |  |  | Dual JK Flip-Flop |
| 443-28 |  |  | CuL995879 |  |  |  |  |  |  |  |  |  |  |  | Decade Counter |
| 443-29 |  |  | CuL995979 |  |  |  |  |  |  |  |  |  |  |  | 4-Bit Buffer-Storage |
| 443-30 |  |  | CuL996079 |  |  |  |  |  |  |  |  |  |  |  | "Nixie" Decoder Driver |
| 443-31 |  |  | MC726P |  |  |  |  |  |  |  |  |  |  |  | Single JK Flip-Flop (RTL) |
| 443-32 |  |  | MC790P |  |  |  |  |  |  |  |  |  |  |  | Dual JK Flip-Flop |
| 443-34 |  |  | 7492N |  |  |  |  |  |  |  |  |  |  |  | 4-bit Counter |
| 443-35 |  |  | 7441N |  |  |  |  |  |  |  |  |  |  |  | BCD to Decimal Decoder 70V |
| 443-36 |  |  | 7447N |  |  |  |  |  |  |  |  |  |  |  | BCD to 7-Segment Decoder |
| 443-37 |  |  | 74100N |  |  |  |  |  |  |  |  |  |  |  | 8-Bit Bi-Stable Latch |
| 443-38 |  |  | MC1023P |  |  |  |  |  |  |  |  |  |  |  | Dual NOR/OR Gate |
| 443-39 |  |  | MC1034 |  |  |  |  |  |  |  |  |  |  |  | Single D Flip-Flop |
| 443-40 |  |  | MC1013P |  |  |  |  |  |  |  |  |  |  |  | Single JK Flip-Flop |
| 443-41 |  |  | MC1027P |
| 443-42 |  |  | 74S112N |  |  |  |  |  |  |  |  |  |  |  | Dual JK Flip-Flop |
| 443-43 |  |  | 74H102N |  |  |  |  |  |  |  |  |  |  |  | JK Flip-Flop |
| 443-44 |  |  | 7413N |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Input NAND (Schm Trig) |
| 443-45 |  |  | 7408N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input AND |
| 443-46 |  |  | 7402N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NOR |
| 443-53 |  |  | 7442N |  |  |  |  |  |  |  |  |  |  |  | 4:10 Line Decoder |
| 443-54 |  |  | 7403N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-input NAND (OC) |
| 443-57 |  |  | MC3003P |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input OR |
| 443-61 |  |  | MC4016P |  |  |  |  |  |  |  |  |  |  |  | Quad Bilateral Switch |
| 443-62 |  |  | MC4044 |  |  |  |  |  |  |  |  |  |  |  | Phase Detector for PLL |
| 443-65 |  |  | 7427 |  |  |  |  |  |  |  |  |  |  |  | Triple 3-Input NOR |
| 443-66 |  |  | 74192N |  |  |  |  |  |  |  |  |  |  |  | Up/Down Decade Counter |
| 443-67 |  |  | MC8601P |  |  |  |  |  |  |  |  |  |  |  | Retrig Monostable |
| 443-70 |  |  | 74H103N |  |  |  |  |  |  |  |  |  |  |  | Dual JK Flip-Flop |
| 443-71 |  |  | 74H00N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-input NAND High Speed |
| 443-72 |  |  | 7417N |  |  |  |  |  |  |  |  |  |  |  | Hex Buffer Driver |
| 443-73 |  |  | 7416N |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter Buffer |
| 443-74 |  |  | 74452 |
| 443-77 |  |  | 7438 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NAND |
| 443-79 |  |  | 95H0359 |  |  | 95H03 |  |  |  |  |  | Trpl 2-Input OR/NOR (180MHz) |
| 443-80 |  |  | MC1035 |  |  |  |  |  |  |  |  |  |  |  | Triple Diff Amp |
| 443-81 |  |  | 95H02 |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Input OR/NOR (180MHz) |
| 443-82 |  |  | 952859 |  |  | 9528 |  |  |  |  |  | Dual D (160MHz) |
| 443-83 |  |  | 95H2859 |  |  | 95H28 |  |  |  |  |  | Dual D-Type Flip-Flop (180MHz) |
| 443-84 |  |  | MK5009 |  |  |  |  |  |  |  |  |  |  |  | Mostek Oscillator Scaler chip |
| 443-85 |  |  | 74157 |  |  | 9322 |  |  |  |  |  | Quad 2-line to 1-line |
| 443-86 |  |  | 9503 |  |  |  |  |  |  |  |  |  |  |  | Trpl 2-Input OR/NOR (160 MHz) |
| 443-87 |  |  | 74145N |  |  |  |  |  |  |  |  |  |  |  | BCD To Decimal Decoder |
| 443-89 |  |  | 7409N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input AND |
| 443-90 |  |  | 74123 |  |  |  |  |  |  |  |  |  |  |  | Dual Retriggerable Monostable |
| 443-94 |  |  | 7483 |  |  |  |  |  |  |  |  |  |  |  | 4-bit full adder |
| 443-95 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 600 MHz Decade Counter |
| 443-98 |  |  | 9582 |  |  |  |  |  |  |  |  |  |  |  | Triple Line Receiver ECL |
| 443-99 |  |  | TMS0101 |  |  |  |  |  |  |  |  |  |  |  | TI Calculator Chip |
| 443-601 |  |  | MK5017AA |  |  |  |  |  |  |  |  |  |  |  | Mostek Clock Chip w/ Alarm |
| 443-602 |  |  | DD700 |  |  | DM8880 |  |  |  |  |  | 7-Segment Decoder Driver |
| 443-603 |  |  | CD4011 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NAND |
| 443-604 |  |  | CD4007AE |  |  |  |  |  |  |  |  |  |  |  | Dual Comp Pair + Inverter |
| 443-606 |  |  | CD4027 |  |  |  |  |  |  |  |  |  |  |  | Dual JK Flip-Flop |
| 443-607 |  |  | CD4013 |  |  | 14013 |  |  |  |  |  | Dual D Flip-Flop |
| 443-612 |  |  | 74193 |  |  |  |  |  |  |  |  |  |  |  | Binary Counter |
| 443-614 |  |  | TIL306 |  |  |  |  |  |  |  |  |  |  |  | Counter/Decoder/Driver/LED |
| 443-615 |  |  | TIL308 |  |  |  |  |  |  |  |  |  |  |  | Decoder/Driver/LED |
| 443-616 |  |  | Custom IC |  |  |  |  |  |  |  |  |  |  |  | TV Clock Display |
| 443-621 |  |  | TMS0119 |  |  |  |  |  |  |  |  |  |  |  | TI Calculator Chip |
| 443-622 |  |  | 74147 |  |  |  |  |  |  |  |  |  |  |  | 10-line to 4-line decoder |
| 443-623 |  |  | 74154 |  |  |  |  |  |  |  |  |  |  |  | 4-line to 16-line decoder |
| 443-624 |  |  | MC1023 |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Input OR/NOR |
| 443-625 |  |  | 74132N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NAND (SchmTrig) |
| 443-626 |  |  | ICL6013 |  |  |  |  |  |  |  |  |  |  |  | DVM Chip |
| 443-628 |  |  | 74196N |  |  |  |  |  |  |  |  |  |  |  | Presettable 4-Bit Binary Cntr |
| 443-629 |  |  | 7490AN |  |  |  |  |  |  |  |  |  |  |  | Decade Counter |
| 443-633 |  |  | 74160 |  |  |  |  |  |  |  |  |  |  |  | Presettable Up/Down Cntr |
| 443-634 |  |  | TMS0116 |  |  |  |  |  |  |  |  |  |  |  | BCD In/Out 4-Funct Calculator |
| 443-635 |  |  | DM8214 |  |  | 54/75153 |  |  |  |  |  | Dual 4-Input (three-state) |
| 443-636 |  |  | MC10116 |  |  |  |  |  |  |  |  |  |  |  | Triple Line Receiver ECL |
| 443-637 |  |  | MK5017BA |  |  |  |  |  |  |  |  |  |  |  | Clock w/ Calendar (not Alarm) |
| 443-638 |  |  | 9310 |  |  |  |  |  |  |  |  |  |  |  | Presettable Up/Down Cntr |
| 443-640 |  |  | 7493AN |  |  |  |  |  |  |  |  |  |  |  | 4-Bit Binary Counter |
| 443-641 |  |  | S1856 |  |  |  |  |  |  |  |  |  |  |  | Clock Chip |
| 443-647 |  |  | CD4046 |  |  |  |  |  |  |  |  |  |  |  | Phase Locked Loop |
| 443-677 |  |  | MC10211 |  |  |  |  |  |  |  |  |  |  |  | ECL Dual 3-Input NOR |
| 443-679 |  |  | MC10131 |  |  |  |  |  |  |  |  |  |  |  | ECL Dual D-Flop ECL |
| 443-680 |  |  | 7495 |  |  |  |  |  |  |  |  |  |  |  | Shift Register |
| 443-683 |  |  | MC10102 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input OR gate ECL |
| 443-687 |  |  | MK5017AA |  |  |  |  |  |  |  |  |  |  |  | Mostek Clock Chip w/ Alarm |
| 443-690 |  |  | UHP491 |
| 443-691 |  |  | 9368 |  |  |  |  |  |  |  |  |  |  |  | 7-Seg Display Driver |
| 443-692 |  |  | MK50254 |  |  |  |  |  |  |  |  |  |  |  | Mostek Clock Chip w/ Alarm |
| 443-694 |  |  | F9368DC |  |  |  |  |  |  |  |  |  |  |  | 7-Segment Decoder Driver Latch |
| 443-695 |  |  | CD4001 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NOR |
| 443-697 |  |  | 74S64 |  |  |  |  |  |  |  |  |  |  |  | 4-2-3-2 And-OR-Invert |
| 443-698 |  |  | 7486N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input Exclusive OR |
| 443-699 |  |  | MM14511 |  |  |  |  |  |  |  |  |  |  |  | Dual BCD Counter |
| 443-701 |  |  | CD4049 |  |  | 14049 |  |  |  |  |  | Hex Inverting Buffer |
| 443-702 |  |  | F3817 |  |  |  |  |  |  |  |  |  |  |  | Clock Chip |
| 443-703 |  |  | CD4001 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NOR |
| 443-704 |  |  | CD4002 |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Input NOR |
| 443-706 |  |  | CD4071 |  |  | 14071 |  |  |  |  |  | Quad 2-Input OR |
| 443-707 |  |  | CD4515 |  |  | MC14515 |  |  |  |  |  | 4 to 16 Line Controller |
| 443-708 |  |  | CD4516 |  |  | MC14516 |  |  |  |  |  | Binary Up/Down Counter |
| 443-709 |  |  | 74C93 |  |  |  |  |  |  |  |  |  |  |  | 4-Bit Binary Counter |
| 443-710 |  |  | MK50240 |  |  |  |  |  |  |  |  |  |  |  | Top Octave Generator |
| 443-711 |  |  | 74LS247 |  |  |  |  |  |  |  |  |  |  |  | BCD-7 Seg OC |
| 443-712 |  |  | MC14025 |  |  |  |  |  |  |  |  |  |  |  | Triple 3-Input NOR |
| 443-713 |  |  | MC14028 |  |  |  |  |  |  |  |  |  |  |  | BCD To Decimal Decoder |
| 443-714 |  |  | 11C01 |  |  |  |  |  |  |  |  |  |  |  | Dual OR/NOR |
| 443-715 |  |  | 11C70 |  |  |  |  |  |  |  |  |  |  |  | Master/Slave D Flip-Flop |
| 443-716 |  |  | 11C05 |  |  |  |  |  |  |  |  |  |  |  | Div By 4 Prescaler 1100 MHz |
| 443-717 |  |  | 74126N |  |  |  |  |  |  |  |  |  |  |  | Quad Buffer |
| 443-719 |  |  | 74LS266 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-input Exclusive OR OC |
| 443-720 |  |  | CD40097 |  |  |  |  |  |  |  |  |  |  |  | TriState Hex Buffer |
| 443-721 |  |  | 2112-2 |  |  |  |  |  |  |  |  |  |  |  | 256 x 4 SRAM |
| 443-722 |  |  | MC8601P |  |  |  |  |  |  |  |  |  |  |  | Retrig Monostable |
| 443-723 |  |  | MC10216 |  |  |  |  |  |  |  |  |  |  |  | Triple Line Receiver |
| 443-724 |  |  | MC10124 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input AND/NAND ECL |
| 443-725 |  |  | MC10125 |  |  |  |  |  |  |  |  |  |  |  | Hex ECL to TTL Translator ECL |
| 443-726 |  |  | MC10138 |  |  |  |  |  |  |  |  |  |  |  | Decade Counter ECL |
| 443-727 |  |  | 96L02 |  |  |  |  |  |  |  |  |  |  |  | Dual Retrig Monostable |
| 443-728 |  |  | 74LS00 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NAND |
| 443-729 |  |  | 74LS13 |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Input NAND |
| 443-730 |  |  | 74LS74 |  |  |  |  |  |  |  |  |  |  |  | Dual D-Flop |
| 443-731 |  |  | 74LS290 |  |  |  |  |  |  |  |  |  |  |  | 4-Bit BCD Ripple Counter |
| 443-732 |  |  | 74LS30 |  |  |  |  |  |  |  |  |  |  |  | Single 8-Input NAND |
| 443-733 |  |  | 74LS293 |  |  |  |  |  |  |  |  |  |  |  | 4-Bit Binary Ripple Counter |
| 443-735 |  |  | MC14512 |  |  |  |  |  |  |  |  |  |  |  | 8-Channel Data Selector |
| 443-736 |  |  | MC14508 |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Bit Latch |
| 443-737 |  |  | MC14518 |  |  |  |  |  |  |  |  |  |  |  | Dual BCD Counter |
| 443-738 |  |  | MC14556 |  |  |  |  |  |  |  |  |  |  |  | Dual 1-4 Decoder |
| 443-740 |  |  | MC1648P |  |  |  |  |  |  |  |  |  |  |  | VCO for PLL |
| 443-743 |  |  | CD40192 |  |  |  |  |  |  |  |  |  |  |  | Up/Down Counter |
| 443-746 |  |  | MC1648P |  |  |  |  |  |  |  |  |  |  |  | VCO for PLL |
| 443-751 |  |  | CD4081 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input AND |
| 443-752 |  |  | 74LS175 |  |  |  |  |  |  |  |  |  |  |  | Quad D-FF |
| 443-753 |  |  | 74S240 |  |  |  |  |  |  |  |  |  |  |  | Octal Buffer Tri-State |
| 443-754 |  |  | 74LS240 |  |  |  |  |  |  |  |  |  |  |  | Octal Buffer Tri-State |
| 443-755 |  |  | 74LS04 |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter |
| 443-757 |  |  | 74LS161 |  |  |  |  |  |  |  |  |  |  |  | 4-Bit Sync Binary Counter |
| 443-760 |  |  | CD4040 |  |  |  |  |  |  |  |  |  |  |  | 12-Bit Binary Ripple Counter |
| 443-761 |  |  | IM6402 |  |  |  |  |  |  |  |  |  |  |  | UART |
| 443-764 |  |  | 2114 |  |  | 4045 |  | 6614 |  | 1k x 4 SRAM |
| 443-765 |  |  | MC10105 |  |  |  |  |  |  |  |  |  |  |  | Triple 2-3-2-Input OR/NOR ECL |
| 443-778 |  |  | CD4093 |  |  | 14093 |  |  |  |  |  | Quad 2-Input NAND Schmidt Trig |
| 443-779 |  |  | 74LS02 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NOR |
| 443-780 |  |  | 74LS08 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input AND |
| 443-781 |  |  | 74LS75 |  |  |  |  |  |  |  |  |  |  |  | Quad D-Flop |
| 443-782 |  |  | 74LS155 |  |  |  |  |  |  |  |  |  |  |  | Dual 1:4 Demux |
| 443-783 |  |  | MC14022 |
| 443-784 |  |  | CD4070 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input Exclusive OR |
| 443-785 |  |  | 74C221 |  |  |  |  |  |  |  |  |  |  |  | Dual Monostable Multivibrator |
| 443-791 |  |  | 74LS244 |  |  |  |  |  |  |  |  |  |  |  | Octal Bus Driver Tri-State |
| 443-792 |  |  | 74LS132 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NAND |
| 443-793 |  |  | 4702 |  |  |  |  |  |  |  |  |  |  |  | Baud Rate Generator |
| 443-794 |  |  | 75188 |  |  | 1488 |  |  |  |  |  | RS-232 Driver |
| 443-795 |  |  | 75189 |  |  | 1489 |  |  |  |  |  | RS-232 Receiver |
| 443-796 |  |  | DM8130 |  |  |  |  |  |  |  |  |  |  |  | 10-Bit Comparator |
| 443-797 |  |  | 74LS10 |  |  |  |  |  |  |  |  |  |  |  | Triple 3-Input NAND |
| 443-798 |  |  | 74LS20 |  |  |  |  |  |  |  |  |  |  |  | Dual 4-input NAND |
| 443-799 |  |  | 74LS157 |  |  |  |  |  |  |  |  |  |  |  | Quad 2 to 1 Multiplexer |
| 443-800 |  |  | 74LS27 |  |  |  |  |  |  |  |  |  |  |  | Triple 3-Input NOR |
| 443-801 |  |  | 74LS196 |  |  |  |  |  |  |  |  |  |  |  | Binary Counter/Latch |
| 443-802 |  |  | 74LS257 |  |  |  |  |  |  |  |  |  |  |  | Quad 2 to 1 line multiplexer |
| 443-803 |  |  | 74273 |  |  |  |  |  |  |  |  |  |  |  | Octal D-Flop |
| 443-804 |  |  | 74LS259 |  |  |  |  |  |  |  |  |  |  |  | 8-Bit Addressable Latch |
| 443-805 |  |  | 74LS273 |  |  |  |  |  |  |  |  |  |  |  | Octal D-Flop |
| 443-807 |  |  | 74LS42 |  |  |  |  |  |  |  |  |  |  |  | BCD to Decimal Decoder |
| 443-808 |  |  | 4N26 |  |  |  |  |  |  |  |  |  |  |  | Opto Coupler |
| 443-811 |  |  | 74LS125 |  |  |  |  |  |  |  |  |  |  |  | Quad Buffer |
| 443-812 |  |  | RO-3-2513/CGR001 |
| 443-813 |  |  | 74LS90 |  |  |  |  |  |  |  |  |  |  |  | Decade Counter |
| 443-815 |  |  | 74LS193 |  |  |  |  |  |  |  |  |  |  |  | 4-Bit Up/Down Counter |
| 443-817 |  |  | 74LS192N |  |  |  |  |  |  |  |  |  |  |  | Up/Down Decade Counter |
| 443-818 |  |  | 74LS05 |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter |
| 443-819 |  |  | 8838 |  |  |  |  |  |  |  |  |  |  |  | Quad Bus Driver |
| 443-822 |  |  | 74LS139 |  |  |  |  |  |  |  |  |  |  |  | Dual 1-To-4 Decoder |
| 443-824 |  |  | 74LS241 |  |  |  |  |  |  |  |  |  |  |  | Octal Bus Driver Tri-State |
| 443-827 |  |  | MC6800P |  |  |  |  |  |  |  |  |  |  |  | 8-Bit Microprocessor |
| 443-828 |  |  | 74LS73 |  |  |  |  |  |  |  |  |  |  |  | Dual JK Flip-Flop |
| 443-829 |  |  | 74LS76 |  |  |  |  |  |  |  |  |  |  |  | Dual JK Flip-Flop |
| 443-836 |  |  | CD4174 |  |  |  |  |  |  |  |  |  |  |  | Hex Latch |
| 443-839 |  |  | 74LS243 |  |  |  |  |  |  |  |  |  |  |  | Quad Bus Transceiver |
| 443-840 |  |  | MC6875 |  |  |  |  |  |  |  |  |  |  |  | 6800 Clock Generator |
| 443-842 |  |  | 1406 |
| 443-848 |  |  | MM5316 |  |  |  |  |  |  |  |  |  |  |  | 4-Digit Non-Mux Clock |
| 443-852 |  |  | 9LS259 |  |  |  |  |  |  |  |  |  |  |  | 8-Bit Addressable Latch |
| 443-855 |  |  | 74LS283 |  |  |  |  |  |  |  |  |  |  |  | Adder |
| 443-856 |  |  | 2350 |  |  |  |  |  |  |  |  |  |  |  | Floppy Disk Controller (?) |
| 443-857 |  |  | 74LS367 |  |  |  |  |  |  |  |  |  |  |  | Hex Buffer / Driver |
| 443-858 |  |  | 7414 |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter |
| 443-863 |  |  | 74LS374 |  |  |  |  |  |  |  |  |  |  |  | Octal D-Flop |
| 443-869 |  |  | DS8629 |  |  |  |  |  |  |  |  |  |  |  | National Div by 100 Prescaler |
| 443-871 |  |  | MC14514 |  |  |  |  |  |  |  |  |  |  |  | 4-Bit Ltch/4-16 Line Decoder |
| 443-874 |  |  | 8250 |  |  |  |  |  |  |  |  |  |  |  | UART |
| 443-875 |  |  | 74LS32 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input Or |
| 443-877 |  |  | 74LS138 |  |  |  |  |  |  |  |  |  |  |  | 3-To-8 Line Decoder |
| 443-879 |  |  | 74LS174 |  |  |  |  |  |  |  |  |  |  |  | Hex D-Flop |
| 443-881 |  |  | Z-80 |  |  |  |  |  |  |  |  |  |  |  | Microprocessor |
| 443-884 |  |  | 74LS242 |  |  |  |  |  |  |  |  |  |  |  | Quad Bus Transceiver Tri-State |
| 443-885 |  |  | 74LS245 |  |  |  |  |  |  |  |  |  |  |  | Octal Bus Transceiver |
| 443-887 |  |  | CD4023 |  |  |  |  |  |  |  |  |  |  |  | Triple 3-Input NAND Buffered |
| 443-891 |  |  | 74LS86 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input Excluxive OR |
| 443-892 |  |  | 74LS166 |  |  |  |  |  |  |  |  |  |  |  | 8-Bit Shift Register |
| 443-896 |  |  | 74S02 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NOR |
| 443-897 |  |  | 74S04 |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter |
| 443-900 |  |  | 74S74 |  |  |  |  |  |  |  |  |  |  |  | Dual D Flip-Flop |
| 443-906 |  |  | MC6845 |  |  |  |  |  |  |  |  |  |  |  | CRT Controller |
| 443-913 |  |  | 5740 |  |  |  |  |  |  |  |  |  |  |  | Keyboard Controller |
| 443-915 |  |  | 74S86 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input Exclusive OR |
| 443-916 |  |  | CD4538 |  |  |  |  |  |  |  |  |  |  |  | Dual Monostable |
| 443-917 |  |  | CD4030AE |  |  |  |  |  |  |  |  |  |  |  | Quad Exclusive OR gate |
| 443-919 |  |  | 74LS126 |  |  |  |  |  |  |  |  |  |  |  | Quad Buffer Tri-State |
| 443-920 |  |  | 74LS85 |  |  |  |  |  |  |  |  |  |  |  | 4-Bit Magnatude Comparator |
| 443-921 |  |  | 74LS390 |  |  |  |  |  |  |  |  |  |  |  | Dual BCD Counter |
| 443-927 |  |  | CD4059 |  |  |  |  |  |  |  |  |  |  |  | Programmable Div by "N" |
| 443-928 |  |  | CD4008B |  |  |  |  |  |  |  |  |  |  |  | 4-Bit Adder |
| 443-929 |  |  | 14017 |  |  |  |  |  |  |  |  |  |  |  | Divide by 10 "Ring Counter" |
| 443-931 |  |  | CD4543 |  |  |  |  |  |  |  |  |  |  |  | 7-Segment Decoder Latch Driver |
| 443-932 |  |  | MC14544 |  |  |  |  |  |  |  |  |  |  |  | 300 Baud Modem |
| 443-933 |  |  | 5101 |  |  | 51L01 |  |  |  |  |  | 256 x 4 RAM |
| 443-935 |  |  | 74S153 |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Input Multiplexer |
| 443-936 |  |  | 7454 |  |  |  |  |  |  |  |  |  |  |  | 8-Input And-Or-Invert |
| 443-937 |  |  | SP8685B |  |  |  |  |  |  |  |  |  |  |  | 512 MHz Divide By 10/11 |
| 443-938 |  |  | ICM7216D |  |  |  |  |  |  |  |  |  |  |  | Frequency counter Chip |
| 443-939 |  |  | MC6808P |  |  | MC6802P |  |  |  |  |  | 8-Bit Microprocessor w/ Clock |
| 443-940 |  |  | SP8647B |
| 443-942 |  |  | 74LS123 |  |  |  |  |  |  |  |  |  |  |  | Dual Retrig Monostable |
| 443-948 |  |  | 74LS112 |  |  |  |  |  |  |  |  |  |  |  | Dual JK Flip-Flop |
| 443-949 |  |  | ADC0804 |  |  |  |  |  |  |  |  |  |  |  | A/D Converter |
| 443-950 |  |  | CD4072 |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Input OR |
| 443-951 |  |  | 74LS51 |  |  |  |  |  |  |  |  |  |  |  | AND/OR Invert |
| 443-952 |  |  | 8250 |  |  |  |  |  |  |  |  |  |  |  | UART |
| 443-953 |  |  | 3880 |  |  | Z80A |  |  |  |  |  | 8-Bit CPU |
| 443-955 |  |  | 74LS153 |  |  |  |  |  |  |  |  |  |  |  | Multiplexer |
| 443-957 |  |  | 14519 |  |  |  |  |  |  |  |  |  |  |  | 4-bit AND/OR select |
| 443-958 |  |  | CD4060 |  |  |  |  |  |  |  |  |  |  |  | 14 Stage Ripple Carry Bin Cntr |
| 443-967 |  |  | 7406N |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter |
| 443-969 |  |  | 74LS196 |  |  |  |  |  |  |  |  |  |  |  | Presettable 4-Bit Binary Cntr |
| 443-973 |  |  | 74LS393 |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Bit Binary Counter |
| 443-987 |  |  | MM5430 |  |  |  |  |  |  |  |  |  |  |  | Frequency Counter Chip |
| 443-992 |  |  | CD4051 |  |  |  |  |  |  |  |  |  |  |  | 8 Channel Analog Mux |
| 443-995 |  |  | SC-01 |  |  | SC-02 (?) |  |  |  |  |  | Votrax Speech Processor |
| 443-996 |  |  | TMS5100 |  |  |  |  |  |  |  |  |  |  |  | LPC Speech Synthesizer |
| 443-1008 |  |  | 74LS221 |  |  |  |  |  |  |  |  |  |  |  | Dual Monostable |
| 443-1014 |  |  | MC68A21P |  |  | MC68B21P |  |  |  |  |  | 8-Bit Dual Peripheral Adapter |
| 443-1016 |  |  | 6116 |  |  |  |  |  |  |  |  |  |  |  | 2k x 8 Static RAM |
| 443-1019 |  |  | MC6850P |  |  |  |  |  |  |  |  |  |  |  | ASYNC Interface Adapter |
| 443-1020 |  |  | 7407N |  |  |  |  |  |  |  |  |  |  |  | Hex Buffer |
| 443-1027 |  |  | 6116 |  |  |  |  |  |  |  |  |  |  |  | 2k x 8 Static RAM |
| 443-1032 |  |  | MK4116-26P |  |  |  |  |  |  |  |  |  |  |  | 16k Dynamic RAM |
| 443-1039 |  |  | 74LS365A |  |  |  |  |  |  |  |  |  |  |  | Hex Buffer / Driver |
| 443-1055 |  |  | MSM5832 |  |  |  |  |  |  |  |  |  |  |  | uP Real-Time Clock (Oki) |
| 443-1060 |  |  | MC1488P |  |  |  |  |  |  |  |  |  |  |  | RS-232 Driver |
| 443-1066 |  |  | D8253C-2 |
| 443-1080 |  |  | 74ALS00 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-input NAND |
| 443-1088 |  |  | AM26LS31PC |  |  |  |  |  |  |  |  |  |  |  | Quad Diff Line Driver |
| 443-1096 |  |  | 74ALS244 |  |  |  |  |  |  |  |  |  |  |  | Octal Buffer Tri-State |
| 443-1099 |  |  | SD4324 |  |  |  |  |  |  |  |  |  |  |  | Fibre Optic Schmitt Detector |
| 443-1109 |  |  | HCPL2531 |  |  |  |  |  |  |  |  |  |  |  | Opto-Coupler |
| 443-1111 |  |  | MC6809 |  |  |  |  |  |  |  |  |  |  |  | 16-Bit uP |
| 443-1117 |  |  | 74LS374 (Selected) |  |  |  |  |  |  |  |  |  |  |  | Octal D-Flop |
| 443-1118 |  |  | MD14518 |  |  |  |  |  |  |  |  |  |  |  | Dual BCD Decoder |
| 443-1123 |  |  | MM5451 |  |  |  |  |  |  |  |  |  |  |  | LED Display Driver |
| 443-1124 |  |  | 74HC393 |  |  |  |  |  |  |  |  |  |  |  | Dual 4-Bit Binary Counter |
| 443-1125 |  |  | 74C165 |  |  |  |  |  |  |  |  |  |  |  | 8-Bit Shift Reg |
| 443-1138 |  |  | 6264 |  |  |  |  |  |  |  |  |  |  |  | 8k x 8 Static RAM |
| 443-1139 |  |  | MC146818P |  |  |  |  |  |  |  |  |  |  |  | CMOS Real-Time Clock |
| 443-1145 |  |  | CD40106 |  |  |  |  |  |  |  |  |  |  |  | Hex Schmidt Trigger |
| 443-1146 |  |  | 14568 |  |  |  |  |  |  |  |  |  |  |  | PLL Phase Detector |
| 443-1147 |  |  | 14526 |  |  |  |  |  |  |  |  |  |  |  | PLL Programmable Divider |
| 443-1149 |  |  | D7201C |
| 443-1150 |  |  | WD1943PD |
| 443-1151 |  |  | 14555 |  |  |  |  |  |  |  |  |  |  |  | Dual 1 of 4 Decoder |
| 443-1155 |  |  | CD4069 |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter |
| 443-1164 |  |  | RC4200 |  |  |  |  |  |  |  |  |  |  |  | Analog Multiplier |
| 443-1175 |  |  | 74HC32 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input OR |
| 443-1188 |  |  | TL851CN |  |  |  |  |  |  |  |  |  |  |  | Polaroid Digital Ranging Cntrl |
| 443-1189 |  |  | ADC0831 |  |  |  |  |  |  |  |  |  |  |  | 8-Bit Serial I/O A/D Converter |
| 443-1196 |  |  | 74ALS1034 |  |  |  |  |  |  |  |  |  |  |  | Hex Buffer |
| 443-1200 |  |  | OKI M205 |
| 443-1201 |  |  | TMS5110A |  |  |  |  |  |  |  |  |  |  |  | LPC Speech Synthesizer |
| 443-1202 |  |  | MC14028 |  |  |  |  |  |  |  |  |  |  |  | BCD To Decimal Decoder |
| 443-1231 |  |  | 74ALS030 |
| 443-1235 |  |  | 74ALS299 |  |  |  |  |  |  |  |  |  |  |  | 8-Bit Universal Shift Reg |
| 443-1239 |  |  | 74ALS138 |  |  |  |  |  |  |  |  |  |  |  | 3-To-8 Line Decoder |
| 443-1259 |  |  | 6522 |  |  |  |  |  |  |  |  |  |  |  | VIA Dual 8-Bit Parallel Port |
| 443-1260 |  |  | 6551 |  |  |  |  |  |  |  |  |  |  |  | UART Controller |
| 443-1261 |  |  | WD1935 |  |  |  |  |  |  |  |  |  |  |  | HDLC Controlller |
| 443-1263 |  |  | 2212 |  |  |  |  |  |  |  |  |  |  |  | NOV-RAM |
| 443-1290 |  |  | 74LS7225 |
| 443-1307 |  |  | 74HC02N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NOR |
| 443-1308 |  |  | 74HC04 |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter |
| 443-1309 |  |  | 74HC74 |  |  |  |  |  |  |  |  |  |  |  | Dual D Flip-Flop |
| 443-1311 |  |  | 74HC138 |  |  |  |  |  |  |  |  |  |  |  | 3-To-8 Line Decoder |
| 443-1313 |  |  | 74HC175N |  |  |  |  |  |  |  |  |  |  |  | Quad D-Flop |
| 443-1315 |  |  | 74ALS05AN |  |  |  |  |  |  |  |  |  |  |  | Hex Inverter |
| 443-1317 |  |  | 74HC27 |  |  |  |  |  |  |  |  |  |  |  | Triple 3-Input NOR |
| 443-1318 |  |  | 74HC125 |  |  |  |  |  |  |  |  |  |  |  | Quad Buffer |
| 443-1319 |  |  | 74HC139 |  |  |  |  |  |  |  |  |  |  |  | Dual 1-To-4 Decoder |
| 443-1321 |  |  | 74HC174N |  |  |  |  |  |  |  |  |  |  |  | Hex D-Flop |
| 443-1322 |  |  | 74HC126N |  |  |  |  |  |  |  |  |  |  |  | Quad Buffer |
| 443-1326 |  |  | 74HC257N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input Mux |
| 443-1327 |  |  | 74HC4078N |  |  |  |  |  |  |  |  |  |  |  | 8-Input NOR |
| 443-1328 |  |  | 74HC298N |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input Mux/DeMux |
| 443-1329 |  |  | 74HC367N |  |  |  |  |  |  |  |  |  |  |  | Hex Tri-State Buffer |
| 443-1330 |  |  | 74HC368N |  |  |  |  |  |  |  |  |  |  |  | Hex Tri-State Inverter |
| 443-1331 |  |  | 74HC373 |  |  |  |  |  |  |  |  |  |  |  | Octal D Latch |
| 443-1332 |  |  | 74HC390N |  |  |  |  |  |  |  |  |  |  |  | Dual BCD Counter |
| 443-1333 |  |  | 74HC652P |  |  |  |  |  |  |  |  |  |  |  | Octal Registered Transceiver |
| 443-1335 |  |  | 74HC515N |
| 443-1338 |  |  | 82C53P-2 |  |  |  |  |  |  |  |  |  |  |  | Prog Interval Timer |
| 443-1344 |  |  | 54HC137 |  |  |  |  |  |  |  |  |  |  |  | 1 of 8 Decoder |
| 443-1362 |  |  | 74HC377 |  |  |  |  |  |  |  |  |  |  |  | Octal "D" Flop |
| 443-1367 |  |  | 74HCT00 |  |  |  |  |  |  |  |  |  |  |  | Quad 2-Input NAND |
| 443-1382 |  |  | 74HC374 |  |  |  |  |  |  |  |  |  |  |  | Octal D Flip-Flop |
| 443-1383 |  |  | 74HC123 |  |  |  |  |  |  |  |  |  |  |  | Dual Retrig Monostable |
| 443-1390 |  |  | 74HC365 |  |  |  |  |  |  |  |  |  |  |  | Hex Buffer Line Driver |
| 443-1391 |  |  | 74HC366 |  |  |  |  |  |  |  |  |  |  |  | Hex Buffer Line Driver |
| 443-1392 |  |  | 84C00-04 |  |  |  |  |  |  |  |  |  |  |  | Z-80 Microprocessor CMOS |
| 443-1393 |  |  | 84C30-04 |  |  |  |  |  |  |  |  |  |  |  | Z-80 Counter/Timer CMOS |
| 443-1394 |  |  | 84C42-04 |  |  |  |  |  |  |  |  |  |  |  | Z-80 Dual Serial Port CMOS |
| 443-1414 |  |  | 74F646N |  |  |  |  |  |  |  |  |  |  |  | Octal Transceiver Register |
| 443-1422 |  |  | 6264 |  |  |  |  |  |  |  |  |  |  |  | 8k x 8 Static RAM |
| 443-1553 |  |  | 6264 |  |  | 5864 |  |  |  |  |  | 8k x 8 Static RAM |
| 443-1703 |  |  | 84C00-06 |  |  |  |  |  |  |  |  |  |  |  | Z-80 Microprocessor CMOS |
| 443-1704 |  |  | 84C30-06 |  |  |  |  |  |  |  |  |  |  |  | Z-80 Counter/Timer CMOS |
| 443-1705 |  |  | 84C42-06 |  |  |  |  |  |  |  |  |  |  |  | Z-80 Dual Serial Port CMOS |
| Programmable Device |
| 444-17 |  |  | MCM6830A ROM |  |  |  |  |  |  |  |  |  |  |  | used in ET-3400 |
| 444-19 |  |  | 2316 |  |  |  |  |  |  |  | 2k x 8 ROM |  | used in H-17 |
| 444-23 |  |  | 3870 uP |  |  | MK14262N-5 |  | New Stock Available |  | used in ID-4001/ID-2090 |
| 444-29 |  |  | 2316 |  |  | 8316 |  | 2k x 8 ROM |  | used in H-19 |
| 444-31 |  |  | 3870 uP |  |  |  |  |  |  |  |  |  |  |  | used in H-14 |
| 444-37 |  |  | 2316 |  |  | 8316 |  | 2k x 8 ROM |  | used in H-19 |
| 444-46 |  |  | 2716 |  |  |  |  |  |  |  | 2k x 8 EPROM |  | used in H-19 |
| 444-69 |  |  | 3870 uP |  |  | MK14623N-5 |  |  |  |  |  | used in SA-5010 |
| 444-76 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | used in ET-3400 |
| 444-80 |  |  | VM61006A |  |  |  |  |  |  |  | Speech ROM |  | used in EE-3403 |
| 444-108 |  |  | D8741A |
| 444-109 |  |  | P3041 |
| 444-110 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | used in Hero-1 (ET-18) |
| 444-141 |  |  | D8741A |
| 444-161 |  |  | MK3870/42 |
| 444-198-1 |  |  | MC68764 |  |  |  |  |  |  |  | 8k x 8 ROM |  | used in Hero-1 (ET-18) |
| 444-199 |  |  | MK3870/42 |
| 444-200-1 |  |  | 3870 uP |  |  |  |  |  |  |  |  |  |  |  | used in GC-1000 WWV Clock |
| 444-205-1 |  |  | 8748 uP |  |  |  |  |  |  |  |  |  |  |  | used in GD-1530 |
| 444-221-1 |  |  | 2732 |  |  | ET-18-4 Utility ROM |  | 4k x 8 ROM |  | used in ET-18 (Option) |
| 444-226 |  |  | 14L8CNS |  |  |  |  |  |  |  | PAL |
| 444-227 |  |  | 12L6CN |
| 444-239-1 |  |  | 2732 |  |  | ET-18-7 Auto Mode |  | 4k x 8 ROM |  | used in ET-18 (Option) |
| 444-240 |  |  | 3870 uP |  |  |  |  |  |  |  |  |  |  |  | used in AD-1308 |
| 444-249 |  |  | PLA |  |  |  |  |  |  |  |  |  |  |  | used in ET-18-6 |
| 444-250 |  |  |  |  |  |  |  |  | System ROM Remote |  |  |  |  |  | used in ET-18-3 |
| 444-254-2 |  |  | MC68A364 ROM |  |  |  |  |  |  |  | 16k x 8 ROM |  | used in RT-18 |
| 444-275 |  |  | VM61006A |  |  |  |  |  |  |  | Speech ROM |  | (See 444-80) |
| 444-283-2 |  |  | MC68A364 ROM |  |  |  |  |  |  |  | 16k x 8 ROM |  | used in RT-18 |
| 444-293-1 |  |  | 3870 uP |  |  |  |  |  |  |  |  |  |  |  | used in GC-1000 WWV Clock |
| 444-295 |  |  | PAL |  |  |  |  |  |  |  |  |  |  |  | used in RT-18 |
| 444-319-1 |  |  | 2764 |  |  | ET-18-9 Hero1 BASIC |  | 8k x 8 ROM |  | used in ET-18 (Option) |
| 444-344-1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | used in 4850 Digital Scope |
| 444-349 |  |  | 2764 |  |  |  |  |  |  |  | 8k x 8 EPROM |  | used in HD-4040 |
| 444-350 |  |  | 2764 |  |  |  |  |  |  |  | 8k x 8 EPROM |  | used in HD-4040 |
| 444-351 |  |  | 2764 |  |  |  |  |  |  |  | 8k x 8 EPROM |  | used in HD-4040 |
| 444-352 |  |  | 2764 |  |  |  |  |  |  |  | 8k x 8 EPROM |  | used in HD-4040 |
| 444-353 |  |  | 74288 |  |  |  |  |  |  |  | FPROM |  | used in HD-4040 |
| 444-449 |  |  | 16R6ACN |  |  |  |  |  |  |  | PAL |
| 444-461 |  |  | 16R8BCN |  |  |  |  |  |  |  | PAL |
| 444-475 |  |  | 27C256 |  |  |  |  |  |  |  | 32k x 8 CMOS EPROM |  | used in ID-5001 |
| 444-852 |  |  | 27C64 |  |  |  |  |  |  |  | 8k x 8 CMOS EPROM |  | used in HC-1032 |
| 444-1010 |  |  | 27C256 |  |  |  |  |  |  |  | 32k x 8 CMOS EPROM |  | used in ID-5001 |
| 444-9006 |  |  | TMS2708JL-45 |  |  |  |  |  |  |  |  |  |  |  | 1024 x 8 EPROM |
| 444-9033 |  |  | MC68764 |  |  |  |  |  |  |  | 8k x 8 ROM |  | used in RT-18 |
| Buy-Sell |
| 643-95 |  |  | HD61604 |  |  |  |  |  |  |  |  |  |  |  | LCD Driver (ID-5001) |
|  | My appreciation to Milton Ferguson for contributing 57 Items to list from his purchase of |
|  | N.O.S. Heathkit Inventory (02/14/2002) Thanks!!!! |
|  | This cross reference is constantly being added to from any additional manuals that I see or acquire. |
|  | Please check it often to stay current. |
|  | If you would like to add an item to this list, send me a copy of the Parts Identification page of your |
|  | manual and I will add the parts. |